## Slide 1: The CDC 8512 Microprocessor
Dr. Charles R. Severance
online.dr-chuck.com

## Slide 2: About the CDC6500
60 bit words – Integer and floating point formats
6 bit characters - upper case only
Two kinds of registers - A0-A7 – Address and X0-X7 data
To load from memory you put the address in A1-A5 and the data from memory is loaded into the corresponding X1-X5
To store into memory you put the data in X6 or X7 and Set the corresponding A6 or A7 to the location where you want the memory stored

## Slide 3
Control Data 6400/6500/660 Computer Systems Reference Manuaal – Figure 3.2
http://ygdes.com/CDC/60100000D_6600refMan_Feb67.pdf
Operating Registers
In order to provide a more compact symbolic language, the 24 operating registers are identified by letters and numbers:
A = Address Register (A0, A1 .. A7)
B = increment register (B0, B1 … B7)
X = operand register (X0, X1 … X7)
The operand registers hold operands and results for servicing the functional units. Five registers (X1-X5)

## Slide 4: CDC8512 Architecture
255
A0
255
X0
255
A1
255
X1
255
A2
255
X2
255
A3
255
X3
L O A D
S T O R E
255
PC
<=>
CM
255
0x00
255
0x01
255
0x02
255
0x03
255
0x04
255
0x05
…
255
0xFD
255
0xFE
255
0xFF
Central Processing Unit
Instruction Memory
255
0x00
255
0x01
255
0x02
255
0x03
255
0x04
255
0x05
…
255
0xFD
255
0xFE
255
0xFF
Data Memory

## Slide 5: Halt Instruction
0
0
0
0
0
0
0
0
HALT # Stop the CPU

## Slide 6: Single Register Instruction
0
1
0
0
1
1
1
0
INC X2 # Add 1 to X2
Register
Number
0 = A register
1 = X register
Register
Increment Register

## Slide 7: Two Byte Instruction
1
0
0
0
1
1
0
0
SX0 0x43 # Set X0
SX0 67 # Set X0
SC0 'C' # Set X0
Register
Number
0 = A register
1 = X register
0x43

## Slide 8: Register to Register Copy
1
1
0
0
1
1
1
1
SX3 A1 # Copy A1 to X3
Register
Number
0 = A register
1 = X register
Register
Number
0 = A register
1 = X register
Source
Register
Destination
Register
Register
Copy