## Slide 1: Solid State Computing
Dr. Charles R. Severance
www.ca4e.com
online.dr-chuck.com

## Slide 2: Outline
The transistor
  Faster than a relay or tube
  Far less heat and electricity
  Far more reliable and long lasting
  No moving parts
Replaced tubes for amplifiers
  Transistor radios
Computing applications – PNP and NPN
  NPN – Conduct with input is high
  PNP – Stop conducting when input is high
Transistor density and scale

## Slide 3: Valves / Tubes / Vacuum Tubes
The first purely electronic devices to store data and do computations were called "Valves" in the UK
  About 1000 times faster than physical relays
Designed to amplify analog signals
Early application long distance analog telephone calls – needed an amplifier every 10 miles or so
Tube was invented in 1912 Dr. Lee Deforest
https://en.wikipedia.org/wiki/Vacuum_tube
+
⏚
Input
Grid
Cathode
Anode
Output

## Slide 4: Building "Digital" Valves / Tubes
The design of tubes could be tweaked so to move quickly from low voltage to high voltage as the input voltage increased
  Voltage low = off
  Voltage high = on
With the correct design, a range of slightly lower input would be lifted on output
Transition
Audio
Amplifier
Digital
"Valve"
Input Voltage
Output Voltage
Regenerate

## Slide 5: Flaws of Valves
Take lots of power per switch / bit
Lots of heat because each tube usually had a heater to make it easier to generate ions
Physically large
Expensive to manufacture
Made a soft humming noise
Soft electronic glow in the dark
https://en.wikipedia.org/wiki/Valve_amplifier

## Slide 6: Transistors
Building a better Triode (Tube)
Three kinds of materials w.r.t electricity
  Conducting like metal
  Insulating like plastic
  Certain crystals were "semi-conductors"
Semi conductors conduct electricity in certain situations
Lot of experimentation with crystal substances like silicon
https://en.wikipedia.org/wiki/Transistor
https://commons.wikimedia.org/wiki/File:1st-Transistor.jpg

## Slide 7: Nobel Prize!
Transistors are constructed by layering crystals with carefully designed impurities
  Silicon with N-Doping
  Silicon with P-Doping
When voltages are applied to the crystals, sub-atomic stuff happens at the boundaries between the different types of crystals that affect the flow of electrons through the crystals
+
⏚
Input
Grid
Cathode
Anode
Output
N
N
P
+
⏚
Input
Base / Gate
Collector
Emitter
Output
https://en.wikipedia.org/wiki/Nobel_Prize_in_Physics

## Slide 8: Building "Digital" Transistors
The design of transistors could be tweaked so to move quickly from low voltage to high voltage as the input voltage increased
  Voltage low = off
  Voltage high = on
With the correct design, a range of slightly lower input would be lifted on output
AI: Difference between a Bipolar Junction Transistor and NMOS transistor
Transition
Audio
Amplifier
Digital
"Valve"
Input Voltage
Output Voltage
Regenerate

## Slide 9: Two Kinds of "Digital" Transistors
If you take a normal amplifier transistor and tune it to be "more on / off" you get an NMOS transistor
  Open until a voltage is applied
  Dominated in early chips
With a bit more work you can make a PMOS transistor
  Closed until a voltage is applied
  Modern chips use CMOS (NMOS and PMOS working together)
Input Voltage
Output Voltage
NMOS
PMOS
https://en.wikipedia.org/wiki/MOSFET
Transition
Notes: PMOS (p-channel metal-oxide-semiconductor) refers to a type of field-effect transistor (FET) where the current flow is carried by positively charged "holes"
NMOS (n-type metal–oxide–semiconductor) refers to a type of field-effect transistor (FET) where the channel between the source and drain is made of n-type semiconductor material

## Slide 10: We use transistors to implement "gates"
When we build digital logic we think in terms of abstractions that we call "gates"
Gates let us think about in 1's and 0's instead of voltages
The simplest gate is a "not" gate where the output is the opposite of the input
It demonstrates a circuit that reacts – like a simple "if" statement
We will build more complex logic circuits
Input | Output
0 | 1
1 | 0
https://en.wikipedia.org/wiki/Inverter_(logic_gate)

## Slide 11: Not gates over time..
NMOS transistors were available much earlier than PMOS
  Power hungry
  Lots of heat
NMOS + PMOS
  Reduced power
  Reduced heat
Power and heat greatly affect chip density
Vdd
out
A
⏚
A
Vdd
out
⏚
Early - NMOS
Modern - CMOS

## Slide 12: Layout a CMOS NOT Gate (Demo)
https://www.ca4e.com/tools/cmos/

## Slide 13: Digital Logic
To design more complex circuits from half-adders to CPUs it is much easier to think in terms of gates than transistors
Gates are an abstraction
  On / OFF or 1 / 0
The basic gates come from mathematical logic (and IF statements)
  Not / And / Or / Exclusive Or
We also talk about gates that can be built with fewer transistors
  NAND / NOR

## Slide 14: Classic Mathematical Logic Gates
A | Q
0 | 1
1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Not
And
Or
Exclusive Or
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Six transistors
Six transistors
Eight transistors
Two transistors

## Slide 15: NAND and NOR Fewer transistors
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND
NOR
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Four transistors
Four transistors
Images: Wikipedia

## Slide 16: Layout a CMOS NAND Gate
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 17: Sneak Peek: Digital Logic Design

## Slide 18: Scale Over Time
Individual transistors connected with other electronics on a "board"
Integrated circuits with a few transistors or gates
https://en.wikipedia.org/wiki/TO-18
https://en.wikipedia.org/wiki/List_of_7400-series_integrated_circuits

## Slide 19: Very Large Scale Integration (VLSI)
2300 transistors manufactured using photo lithography
The Intel 4004(1971), was first microprocessor you could buy
https://en.wikipedia.org/wiki/Intel_4004
4mm
3mm

## Slide 20: Photo Lithography
https://en.wikipedia.org/wiki/Photolithography
https://en.wikipedia.org/wiki/Photomask
https://en.wikipedia.org/wiki/Semiconductor_device_fabrication
Four Input NAND
Seven transistors
TI 7420
Multiple masks with
different chemicals

## Slide 21: Growth of transistor count
The Intel Itanium was the first billion-transistor chip in 2001
Deep learning wafer scale engine by Cerebras has 2.6 trillion MOSFETs 2020
2 Terabyte flash memory with 5.3 trillion floating-gate MOSFETs
Nvidia's Blackwell-based B100 GPU with 208 billion MOSFETs in 2024
https://en.wikipedia.org/wiki/Transistor_count

## Slide 22: Lets do some VLSI design

## Slide 23: VLSI CMOS Not
Vdd
out
A
⏚
A | Q
0 | 1
1 | 0
Not

## Slide 24: VLSI Layers – Photo Lithography

## Slide 25: VLSI CMOS NAND
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 26: VLSI CMOS NAND
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 27: Summary

## Slide 28: Acknowledgements / Contributions
These slides are Copyright 2025- Charles R. Severance (online.dr-chuck.com) as part of www.ca4e.com and made available under a Creative Commons Attribution 4.0 License. Please maintain this last slide in all copies of the document to comply with the attribution requirements of the license. If you make a change, feel free to add your name and organization to the list of contributors on this page as you republish the materials.
Initial Development: Charles Severance, University of Michigan School of Information
Insert new Contributors and Translators here including names and dates
Continue new Contributors and Translators here