## Slide 1: Solid State Computing
Dr. Charles R. Severance
www.ca4e.com
online.dr-chuck.com

## Slide 2: Outline
The transistor
  Faster than a relay or tube
  Far less heat and electricity
  Far more reliable and long lasting
  No moving parts
Replaced tubes for amplifiers
  Transistor radios
Computing applications – PNP and NPN
  NPN – Conduct with input is high
  PNP – Stop conducting when input is high
Transistor density and scale

## Slide 3: Valves / Tubes / Vacuum Tubes
The first purely electronic devices to store data and do computations were called "Valves" in the UK
  About 1000 times faster than physical relays
Designed to amplify analog signals
Early application long distance analog telephone calls – needed an amplifier every 10 miles or so
Tube was invented in 1912 Dr. Lee De Forest
https://en.wikipedia.org/wiki/Vacuum_tube
+
⏚
Input
Grid
Cathode
Anode
Output

## Slide 4: Building "Digital" Valves / Tubes
The design of tubes could be tweaked so to move quickly from low voltage to high voltage as the input voltage increased
  Voltage low = off
  Voltage high = on
With the correct design, a range of slightly lower input would be lifted on output
Transition
Audio
Amplifier
Digital
"Valve"
Input Voltage
Output Voltage
Regenerate
Notes: The diagram on this page shows a graph of input voltage and output voltage comparing the response of an amplifier type tube to a tube that is designed more for digital applications (0/1). The amplifier graph starts low and then is a curve going up almost linearly over the range of the input voltage. The digital curve stays low longer and then goes up more vertically before tapering off at the top of the output voltage. The concept is that the transition from low to high if gradual and almost linear for the amplifier and quick and almost vertical for the tube tuned for digital applications. The digital tube goes "vertical" at about the 1/3 point of the input voltage – this means that the tub "pulls up" low non-zero voltages like 0.3 to 1 on output.

## Slide 5: Flaws of Valves
Take lots of power per switch / bit
Lots of heat because each tube usually had a heater to make it easier to generate ions
Physically large
Expensive to manufacture
Made a soft humming noise
Soft electronic glow in the dark
https://en.wikipedia.org/wiki/Valve_amplifier

## Slide 6: Semi-Conductors

## Slide 7: Transistors
Building a better Triode (Tube)
Three kinds of materials w.r.t electricity
  Conducting like metal
  Insulating like plastic
  Semi-conductor
Certain crystalline materials like silicon can be modified by adding impurities (‘doping’) so they conduct electricity under certain conditions — hence, semiconductors.
https://en.wikipedia.org/wiki/Transistor
https://commons.wikimedia.org/wiki/File:1st-Transistor.jpg

## Slide 8: Nobel Prize!
Transistors are constructed by layering crystals with carefully designed impurities
  Silicon with N-Doping
  Silicon with P-Doping
When voltages are applied to the crystals, sub-atomic stuff happens at the boundaries between the different types of crystals that affect the flow of electrons through the crystals
+
⏚
Input
Grid
Cathode
Anode
Output
N
N
P
+
⏚
Input
Base / Gate
Collector
Emitter
Output
https://en.wikipedia.org/wiki/Nobel_Prize_in_Physics

## Slide 9: Transistor audio amplifiers – not so simple
A typical transistor amplifier (whether NMOS or BJT) inverts the signal — so an additional stage is used to restore phase.
A few more transistors improve the quality of the amplified signal.
https://en.wikipedia.org/wiki/Amplifier
Input
Output
Notes: BJT – Bipolar Junction Tranistor

## Slide 10: Transistor Radios
Once amplifier style transistors were available, during the 1940's there was an effort to build small, battery-powered "transistor radios"
Often the marketing included the number of transistors – "The Sony TR-826 radio has eight transistors!"
https://en.wikipedia.org/wiki/Transistor_radio

## Slide 11: Hi End Tube-Based Audio Amplifiers
Many and professional musical performers feel that that amplifiers that use tubes produce better sound with less distortion
New high-end audio amplifiers can cost upwards of $50,000
This is not an audio class - so back to digital logic
https://en.wikipedia.org/wiki/Valve_amplifier
Macintosh MC240 - $3500

## Slide 12: Building "Digital" Transistors
The design of transistors could be tweaked to move quickly from high voltage to low voltage as the input voltage increased
  Voltage low = off
  Voltage high = on
With the right design, a range of slightly lower input would be corrected on output
AI: Difference between a Bipolar Junction Transistor and NMOS transistor
Transition
Bipolar
Junction
Transistor
NMOS
Transistor
Input Voltage
Output Voltage
Notes: This is the transistor equivalent of the tube diagram a few slides back. The diagram on this page shows a graph of input voltage and output voltage comparing the response of an amplifier type transistor to a transistor that is designed more for digital applications (0/1). The amplifier graph starts low and then is a curve going up almost linearly over the range of the input voltage. The digital curve stays low longer and then goes up more vertically before tapering off at the top of the output voltage. The concept is that the transition from low to high if gradual and almost linear for the amplifier and quick and almost vertical for the transistor tuned for digital applications. The digital tube goes "vertical" at about the 1/3 point of the input voltage – this means that the transistor "pulls up" low non-zero voltages like 0.3 to 1 on output.

## Slide 13: Two Kinds of "Digital" Transistors
NMOS conducts when the input (gate) voltage is high
PMOS conducts when the input is low.
Modern chips use both
CMOS – Complementary Metal-Oxide-Semiconductor
NMOS
PMOS
https://en.wikipedia.org/wiki/MOSFET
Output Voltage
Input Voltage
Transition
Notes: PMOS (p-channel metal-oxide-semiconductor) refers to a type of field-effect transistor (FET) where the current flow is carried by positively charged "holes"
NMOS (n-type metal–oxide–semiconductor) refers to a type of field-effect transistor (FET) where the channel between the source and drain is made of n-type semiconductor material
The graph on this slide shows an PMOS S-curve going from low to high output voltage with an almost vertical transition at the 2/3 point in the input voltage. The 2/3 point helps pull up voltages that might not quite be 1 on input to 1 on output. The NMOS S-Curve goes from high to low with an almost vertical drop at about the 1/3 point in the input voltage. The 2/3 point helps pull down voltages that might not quite be 1 on input to be 0 on output.
Early logic used PMOS or NMOS depending on what was most effective to manufacture. But the mid 1980s – both NMOS and PMOS could be manufactured in one chip, leading the the use of both on modern chips – we called it CMOS – Complementary Metal-Oxide-Semiconductor. In short NMOS + PMOS = CMOS

## Slide 14: The Four Eras of Transistor Manufacturing
Approx. Years | Dominant Technology | Key Feature | Processors | Limitation that Led to Next Step
1950s–1960s | Bipolar Junction Transistor (BJT) | Fast and well-understood |  | Power-hungry, hard to integrate
Late 1960s–early 1970s | PMOS | Easier to fabricate MOS logic | Intel 4004 | Slow, used negative voltages
1973–1983 | NMOS | Faster, simpler power supply | Intel 8080 Zilog Z-80 | Still wasted static power
1983–present | CMOS | Extremely low power, scalable | Intel 486 | Became universal
ChatGPT: Describe the historical timeline for the transition from Bipolar Junction Transistor (BPT) to Complementary Metal-Oxide-Semiconductor (CMOS) transistor technology.

## Slide 15: Digital Logic and Gates

## Slide 16: We use transistors to implement "gates"
When we build digital logic we think in terms of abstractions that we call "gates"
Gates let us think about in 1's and 0's instead of voltages
The simplest gate is a "not" gate where the output is the opposite of the input
It demonstrates a circuit that reacts – like a simple "if" statement
We will build more complex logic circuits
Input | Output
0 | 1
1 | 0
https://en.wikipedia.org/wiki/Inverter_(logic_gate)

## Slide 17: Not gates over time..
Vdd
out
A
⏚
NMOS - 1978
CMOS - 1983
PMOS - 1972
⏚
A
out
Vdd
A
Vdd
out
⏚
Notes: These not gates show an evolution. In the early 1970s, were easier to manufacture but they were slow and had low density. When the input to a PMOS Not gate is 1 the gate closes, and the output voltage of the transistor is split between the output going to the next gate and the resistor connected to ground. Because of this, the output voltage needs to be "pulled up" by the next gate and the resistor generates heat if the PMOS input is 1. In the late 1970's when manufacturing improved, NMOS transistors could be built with much higher densities. When the input to a NMOS Not gate is 0, the transistor is open (not conducting) and the voltage flows from VCC to the output (1). When the input to the NMOS Not gate is 1, the transistor is closed (conducting) so the output is pulled to ground. Once the transistor is closed current flows directly from VCC to ground and to avoid a short circuit, there is a resistor to limit current from VCC to ground. While the input to the NMOS Not gate is 1, the resistor is using power and generating heat. In Complementary Metal-Oxide-Semiconductor (CMOS) there is both PMOS and NMOS transistors connected to the same input. If the CMOS Not input is zero, the PMOS transistor opens and the NMOS transistor closes and VCC is connected to output with no need for a resistor. When The CMOS Not input is 1, the PMOS transistor closes and the NMOS transistor opens, drawing the output down to (0). CMS Not gates consume very little power and generate very little heat when the input is not changing. There is some heat generated which the input is changing, but overall, the two-transistor CMOS approach uses far less power and generates far less hear than either of the single transistor Not gates. CMOS can handle far greater densities and switching speeds without damage and continues to be the dominate approach in modern chips.

## Slide 18: Not gates over time..
Vdd
out
A
⏚
NMOS - 1978
CMOS - 1983
PMOS - 1972
⏚
A
out
Vdd
A
Vdd
out
⏚
0
1
0
1
🚫
0
🚫
1
♨️
❄
❄
Notes: These not gates show an evolution. In the early 1970s, were easier to manufacture but they were slow and had low density. When the input to a PMOS Not gate is 1 the gate closes, and the output voltage of the transistor is split between the output going to the next gate and the resistor connected to ground. Because of this, the output voltage needs to be "pulled up" by the next gate and the resistor generates heat if the PMOS input is 1. In the late 1970's when manufacturing improved, NMOS transistors could be built with much higher densities. When the input to a NMOS Not gate is 0, the transistor is open (not conducting) and the voltage flows from VCC to the output (1). When the input to the NMOS Not gate is 1, the transistor is closed (conducting) so the output is pulled to ground. Once the transistor is closed current flows directly from VCC to ground and to avoid a short circuit, there is a resistor to limit current from VCC to ground. While the input to the NMOS Not gate is 1, the resistor is using power and generating heat. In Complementary Metal-Oxide-Semiconductor (CMOS) there is both PMOS and NMOS transistors connected to the same input. If the CMOS Not input is zero, the PMOS transistor opens and the NMOS transistor closes and VCC is connected to output with no need for a resistor. When The CMOS Not input is 1, the PMOS transistor closes and the NMOS transistor opens, drawing the output down to (0). CMS Not gates consume very little power and generate very little heat when the input is not changing. There is some heat generated which the input is changing, but overall, the two-transistor CMOS approach uses far less power and generates far less hear than either of the single transistor Not gates. CMOS can handle far greater densities and switching speeds without damage and continues to be the dominate approach in modern chips.

## Slide 19: Not gates over time..
Vdd
out
A
⏚
NMOS - 1978
CMOS - 1983
PMOS - 1972
⏚
A
out
Vdd
A
Vdd
out
⏚
1
0
1
0
🚫
1
🚫
0
♨️
❄
❄
Notes: These not gates show an evolution. In the early 1970s, were easier to manufacture but they were slow and had low density. When the input to a PMOS Not gate is 1 the gate closes, and the output voltage of the transistor is split between the output going to the next gate and the resistor connected to ground. Because of this, the output voltage needs to be "pulled up" by the next gate and the resistor generates heat if the PMOS input is 1. In the late 1970's when manufacturing improved, NMOS transistors could be built with much higher densities. When the input to a NMOS Not gate is 0, the transistor is open (not conducting) and the voltage flows from VCC to the output (1). When the input to the NMOS Not gate is 1, the transistor is closed (conducting) so the output is pulled to ground. Once the transistor is closed current flows directly from VCC to ground and to avoid a short circuit, there is a resistor to limit current from VCC to ground. While the input to the NMOS Not gate is 1, the resistor is using power and generating heat. In Complementary Metal-Oxide-Semiconductor (CMOS) there is both PMOS and NMOS transistors connected to the same input. If the CMOS Not input is zero, the PMOS transistor opens and the NMOS transistor closes and VCC is connected to output with no need for a resistor. When The CMOS Not input is 1, the PMOS transistor closes and the NMOS transistor opens, drawing the output down to (0). CMS Not gates consume very little power and generate very little heat when the input is not changing. There is some heat generated which the input is changing, but overall, the two-transistor CMOS approach uses far less power and generates far less hear than either of the single transistor Not gates. CMOS can handle far greater densities and switching speeds without damage and continues to be the dominate approach in modern chips.

## Slide 20: TL;DR – Not Gates Over Time
Before the 1980's, logic gates built from transistors were slow, had low density, took a lot of heat and took a lot of power.
When CMOS was practical in the 1980s, CPUS went from the size of large cabinets to single chips
As size reduced things got much faster
From now on we will only speak of CMOS 
Vdd
out
A
⏚

## Slide 21: Layout a CMOS NOT Gate (Demo)
https://www.ca4e.com/tools/cmos/

## Slide 22: Digital Logic
To design more complex circuits from half-adders to CPUs it is much easier to think in terms of gates than transistors
Gates are an abstraction
  On / OFF or 1 / 0
The basic gates come from mathematical logic (and IF statements)
  Not / And / Or / Exclusive Or
We also talk about gates that can be built with fewer transistors
  NAND / NOR

## Slide 23: Classic Mathematical Logic Gates
A | Q
0 | 1
1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Not
And
Or
Exclusive Or
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Six transistors
Six transistors
Eight transistors
Two transistors

## Slide 24: NAND and NOR Fewer transistors
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND
NOR
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Four transistors
Four transistors
Images: Wikipedia

## Slide 25: Layout a CMOS NAND Gate
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 26: Sneak Peek: Digital Logic Design

## Slide 27: Increasing Transistor Count

## Slide 28: Scale Over Time
Individual transistors connected with other electronics on a "board"
Integrated circuits with a few transistors or gates
https://en.wikipedia.org/wiki/TO-18
https://en.wikipedia.org/wiki/List_of_7400-series_integrated_circuits

## Slide 29: Very Large Scale Integration (VLSI)
2300 NMOS transistors manufactured using photo lithography
The Intel 4004(1971), was first microprocessor you could buy
https://en.wikipedia.org/wiki/Intel_4004
4mm
3mm

## Slide 30: Photo Lithography
https://en.wikipedia.org/wiki/Photolithography
https://en.wikipedia.org/wiki/Photomask
https://en.wikipedia.org/wiki/Semiconductor_device_fabrication
Four Input NAND
Seven transistors
TI 7420
Multiple masks with
different chemicals

## Slide 31: Growth of transistor count
The Intel Itanium was the first billion-transistor chip in 2001
Deep learning wafer scale engine by Cerebras has 2.6 trillion MOSFETs 2020
2 Terabyte flash memory with 5.3 trillion floating-gate MOSFETs
Nvidia's Blackwell-based B100 GPU with 208 billion MOSFETs in 2024
https://en.wikipedia.org/wiki/Transistor_count

## Slide 32: Very Large Scale Integration (VLSI) Layout

## Slide 33: VLSI CMOS Not
Vdd
out
A
⏚
A | Q
0 | 1
1 | 0
Not

## Slide 34: VLSI Layers – Photo Lithography

## Slide 35: VLSI CMOS NAND
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 36: VLSI CMOS NAND
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 37: Summary
Semiconductors
Tuning tubes and transistor for digital applications (as compared to amplifier applications)
Building gates from transistors
Implementations using NMOS and CMOS logic (heat and power)
Number of transistors on a chip over time
Photo lithography
Designing VLSI chips

## Slide 38: Acknowledgements / Contributions
These slides are Copyright 2025- Charles R. Severance (online.dr-chuck.com) as part of www.ca4e.com and made available under a Creative Commons Attribution 4.0 License. Please maintain this last slide in all copies of the document to comply with the attribution requirements of the license. If you make a change, feel free to add your name and organization to the list of contributors on this page as you republish the materials.
Initial Development: Charles Severance, University of Michigan School of Information
Insert new Contributors and Translators here including names and dates
Continue new Contributors and Translators here