## Slide 1: Digital Logic and Processor Design
Dr. Charles R. Severance
www.ca4e.com
online.dr-chuck.com

## Slide 2: Outline
Computer Architecture
What is a Central Processing Unit (CPU)
We can build VLSI chips with millions of transistors …
Start with gates - AND / OR / NOT / XOR …
Adding numbers with gates – half and full adders
Number representation – Base 2 and Base 16 (hexadecimal)
Storing data with gates – Latches and Flip-Flops
Programming with gates – machine code (0's and 1's)

## Slide 3: Computer Architecture
Within the computer data is moved using electric wires
Each wire generally has a voltage that is either a "0" or "1"
Wires connect components like the CPU, Memory, or other devices
https://en.wikipedia.org/wiki/Printed_circuit_board
A sound chip from a 1980's
Commodore 64 connected to the
motherboard

## Slide 4
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
From: Python for Everybody (www.py4e.com)

## Slide 5: Definitions
Central Processing Unit: Runs the Program - The CPU is always wondering “what to do next”. Not the brains exactly - very dumb but very very fast
Input Devices: Keyboard, Mouse, Touch Screen
Output Devices: Screen, Speakers, Printer, DVD Burner
Main Memory: Fast small temporary storage - lost on reboot - aka RAM
Secondary Memory: Slower large permanent storage - lasts until deleted - disk drive / memory stick
What
Next?

## Slide 6
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
if x< 3: print
From: Python for Everybody (www.py4e.com)

## Slide 7
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001

## Slide 8: Building Microprocessors

## Slide 9: Very Large Scale Integration
We went from 16 transistors on a board 4 inches on a side to billions of transistors in a chip 0.5 inches on a side

## Slide 10: CPU Design Process
We start with gates and build reusable components and then combine those components to implement programmable digital logic
Software translates our abstract design into transistors and then creates an optimal layout for our chip
Photo lithography is then used to build the chip

## Slide 11: Adding numbers with gates

## Slide 12: Classic Mathematical Logic Gates
A | Q
0 | 1
1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Not
And
Or
Exclusive Or
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 13: Representing Larger Numbers with 0's and 1's
If we are going to do significant computations, we will need a way to represent numbers as electrical values
The answer is Base-2 numbers
"Normal" numbers are Base-10
We know the place values of Base-10 numbers
Base-10
12310 = 1 x 102 + 2 x 101 + 3 * 100
= 1 x 100 + 2 * 10 * 3 * 1 = 12310
Base-8
4568 = 4 x 82 + 5 * 81 + 6 * 80
= 4 * 64 + 5 * 8 + 6 * 1 = 17410
Base-2
10112 = 1 * 23 + 1 * 21 + 1*20 =
8 + 2 + 1 = 1110

## Slide 14: Keep it simple for now
Base–2 to Base-10 for numbers less than 8
A.k.a. 3-bit numbers
Base-10 | Base-2
0 | 0
1 | 1
2 | 10
3 | 11
4 | 100
5 | 101
6 | 110
7 | 111
1 1 0 = 6
4 2 1

## Slide 15: Nixie Tubes – Binary to Decimal Display
1 1 0 = 6
4 2 1
https://en.wikipedia.org/wiki/Nixie_tube

## Slide 16: Base-2 Math
1
+ 1
1 0 (2)
1 0 (2)
+ 1 0 (2)
1 0 0 (4)
1 0 0 (4)
+ 1 0 0 (4)
1 0 0 0 (8)
1 1 (3)
+ 1 (3)
1 0 0 (4)
1 1 (3)
+ 1 0 (2)
1 0 0 (5)
1 1 1 (7)
+ 1 (1)
1 0 0 0 (8)

## Slide 17: Half Adder
Compute the sum of two base-2 digits and produce a sum and carry.
HALF
Adder
A
B
SUM
Carry
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 18: Half Adder
Compute the sum of two base-2 digits and produce a sum and carry.
HALF
Adder
A
B
SUM
Carry
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 19: Full Adder
Adds three 0/1 numbers for a sum/carry between 0 and 3
Carry in | A | B | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
1
1
+ 1
1 1 (3)
FULL
Adder
A
B
SUM
Carry out
Carry In

## Slide 20: Full Adder
Adds three 0/1 numbers for a sum/carry between 0 and 3
1
0
+ 1
1 0 (2)

## Slide 21: Chaining full adders
0 1 0 (2)
+ 1 0 1 (5)
1 1 1 (7)

## Slide 22: Three Bit Adder Component
Once we know how to make something, add a component to our design system
0 1 0 (2)
+ 1 0 1 (5)
1 1 1 (7)

## Slide 23: Speed / Delay / Clocks
Latches and Flip-Flops

## Slide 24: Delay
The "longer" a circuit is, the longer it takes for the outputs to "settle" to their final values
Full Adder

## Slide 25: Circuits can get quite long
CI
A
B
S
CO
CI
A
B
S
CO
CI
A
B
S
CO
CI
A
B
S
CO
4 bit adder
32 bit adder
64 bit adder?
64 bit multiplier?

## Slide 26
64 Bit
Adder
Once a circuit is designed and laid out, circuit simulators can compute the time it takes for signals to propagate through the circuit. We can not trust at the results to be accurate until sufficient time has passed.

## Slide 27: Clock Rate
Once we compute the delay of the slowest element of the Arithmetic and Logic parts of the CPU (aka the ALU), we can determine the number of times per second we can reliably do computations.

## Slide 28: Moore's Law
Moore's law is the observation that the number of transistors in an integrated circuit (IC) doubles about every two years.
X-Axis 1970 - 2020
Y-Axis 1000 - 50 billion
https://en.wikipedia.org/wiki/Moore%27s_law

## Slide 29: What Determines Clock Rate?
The size of the chip (speed of light)
The number of transistors in the longest path within the ALU
The physical length of the longest path within the ALU (speed of light)
The speed at which each transistor switches between 0 and 1 (depends on the technology used to build the chip)
Chips are designed, redesigned, laid out, and simulated endlessly during development to produce the fastest clock rate

## Slide 30: Back to Four Bits
Perhaps you wondered where the data to add comes from and where the results are stored so they can be used for a later computation
Like "variables" but inside the CPU
We call them "Registers"
They are built using circuits we call "Flip-Flops"
4 Bit
Adder
https://en.wikipedia.org/wiki/Flip-flop_(electronics)
https://en.wikipedia.org/wiki/Processor_register
Registers

## Slide 31: Storing data with gates
Latches and Flip-Flops

## Slide 32: Programming with gates
Machine code programming in (0's and 1's)