## Slide 1: Digital Logic and Processor Design
Dr. Charles R. Severance
www.ca4e.com
online.dr-chuck.com

## Slide 2: Outline
Computer Architecture
What is a Central Processing Unit (CPU)
We can build VLSI chips with millions of transistors …
Start with gates - AND / OR / NOT / XOR …
Mathematical operations – half and full adders
Storing data – Latches and Flip-Flops
Programmable computations using machine code instructions

## Slide 3: Computer Architecture
Within the computer data is moved using electric wires
Each wire generally has a voltage that is either a "0" or "1"
Wires connect components like the CPU, Memory, or other devices
https://en.wikipedia.org/wiki/Printed_circuit_board
A sound chip from a 1980's
Commodore 64 connected to the
motherboard

## Slide 4
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
From: Python for Everybody (www.py4e.com)

## Slide 5: Definitions
Central Processing Unit: Runs the Program - The CPU is always wondering “what to do next”. Not the brains exactly - very dumb but very very fast
Input Devices: Keyboard, Mouse, Touch Screen
Output Devices: Screen, Speakers, Printer, DVD Burner
Main Memory: Fast small temporary storage - lost on reboot - aka RAM
Secondary Memory: Slower large permanent storage - lasts until deleted - disk drive / memory stick
What
Next?

## Slide 6
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
if x< 3: print
From: Python for Everybody (www.py4e.com)

## Slide 7
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001

## Slide 8: Building Microprocessors

## Slide 9: Very Large Scale Integration
We went from 16 transistors on a board 4 inches on a side to billions of transistors in a chip 0.5 inches on a side

## Slide 10: CPU Design Process
We start with gates and build reusable components and then combine those components to implement programmable digital logic
Software translates our abstract design into transistors and then creates an optimal layout for our chip
Photo lithography is then used to build the chip

## Slide 11: Starting with gates

## Slide 12: Classic Mathematical Logic Gates
A | Q
0 | 1
1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Not
And
Or
Exclusive Or
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 13: Mathematical Operations

## Slide 14: Storing Data

## Slide 15: Machine Language