## Slide 1: Computer Architecture
Dr. Charles R. Severance
www.ca4e.com
online.dr-chuck.com

## Slide 2: Outline
What is Computer Architecture
What is a Central Processing Unit (CPU)
Start with gates - AND / OR / NOT / XOR …
Adding numbers with gates – half and full adders
Number representation – Base 2 and Base 10 (hexadecimal)
Storing data with gates – Latches and Flip-Flops
Speed / Delay / Clocks
Programming with gates – machine code (0's and 1's)
Inside of a CPU

## Slide 3: Computer Architecture
Within the computer data is moved using electric wires
Each wire generally has a voltage that is either a "0" or "1"
Wires connect components like the CPU, Memory, or other devices
https://en.wikipedia.org/wiki/Printed_circuit_board
A sound chip from a 1980's
Commodore 64 connected to the
motherboard

## Slide 4
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
From: Python for Everybody (www.py4e.com)

## Slide 5: Definitions
Central Processing Unit: Runs the Program - The CPU is always wondering “what to do next”. Not the brains exactly - very dumb but very very fast
Input Devices: Keyboard, Mouse, Touch Screen
Output Devices: Screen, Speakers, Printer, DVD Burner
Main Memory: Fast small temporary storage - lost on reboot - aka RAM
Secondary Memory: Slower large permanent storage - lasts until deleted - disk drive / memory stick
What
Next?

## Slide 6
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
if x< 3: print
From: Python for Everybody (www.py4e.com)
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 7
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 8: Building Microprocessors

## Slide 9: Very Large Scale Integration
We went from 16 transistors on a board 4 inches on a side to billions of transistors in a chip 0.5 inches on a side

## Slide 10: CPU Design Process
We start with gates and build reusable components and then combine those components to implement programmable digital logic
Software translates our abstract design into transistors and then creates an optimal layout for our chip
Photo lithography is then used to build the chip

## Slide 11: Adding numbers with gates
Gates are now our low-level building blocks – we can combine them to solve problems

## Slide 12: Classic Mathematical Logic Gates
A | Q
0 | 1
1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Not
And
Or
Exclusive Or
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 13: Representing Numbers with 0's and 1's
If we are going to do significant computations, we will need a way to represent numbers as electrical values
"Normal" numbers are Base-10
We know the place values of Base-10 numbers
To manipulate numbers with gates, we use Base-2 numbers
Base-10
12310 = 1 x 102 + 2 x 101 + 3 * 100
= 1 x 100 + 2 * 10 + 3 * 1 = 12310
Base-2
1102 = 1 * 22 + 1 * 21 + 0*20 =
= 4 + 2 + 0 = 610

## Slide 14: Keep it simple for now
Base–2 to Base-10 for numbers less than 8
A.k.a. 3-bit numbers
Base-10 | Base-2
0 | 0
1 | 1
2 | 10
3 | 11
4 | 100
5 | 101
6 | 110
7 | 111
1 1 0 = 6
4s 2s 1s

## Slide 15: Nixie Tubes – Binary to Decimal Display
1 1 0 = 6
4 2 1
https://en.wikipedia.org/wiki/Nixie_tube

## Slide 16
https://www.ca4e.com/tools/nixie/

## Slide 17: Base-2 Math
1 (1)
+ 1 (1)
1 0 (2)
1 0 (2)
+ 1 0 (2)
1 0 0 (4)
1 0 0 (4)
+ 1 0 0 (4)
1 0 0 0 (8)
1 1 (3)
+ 1 (1)
1 0 0 (4)
1 1 (3)
+ 1 0 (2)
1 0 1 (5)
1 1 1 (7)
+ 1 (1)
1 0 0 0 (8)

## Slide 18: Half Adder
Compute the sum of two base-2 digits and produce a sum and carry.
HALF
Adder
A
B
SUM
Carry
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 19: Half Adder
Compute the sum of two base-2 digits and produce a sum and carry.
HALF
Adder
A
B
SUM
Carry
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 20: Full Adder
Adds three 0/1 numbers for a sum/carry between 0 and 3
Carry in | A | B | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
1 (CIN)
1 (A)
+ 1 (B)
1 1 (3)
FULL
Adder
A
B
SUM
Carry out
Carry In

## Slide 21: Full Adder
Adds three 0/1 numbers for a sum/carry between 0 and 3
1 (CIN)
0 (A)
+ 1 (B)
1 0 (2)
Notes: A diagram of a full adder circuit with inputs A and B with a Carry-In of CIN. The output is single bit SUM and a single but Carry Out. The circuit consisted of two half adders connected and an OR gate to compute the carry out when all the inputs are 1.

## Slide 22: Chaining full adders
0 1 0 (2)
+ 1 0 1 (5)
1 1 1 (7)

## Slide 23: Three Bit Adder Component
Once we know how to make something, add a component to our design system
0 1 0 (2)
+ 1 0 1 (5)
1 1 1 (7)

## Slide 24: Storing data with gates
Latches and Flip-Flops

## Slide 25: Storing Data Using Feedback Loops
The simplest latch is a "Set-Reset" latch using two NOR gates
The output of each NOR gate is connected to the one of the inputs of the other NOR gate
https://en.wikipedia.org/wiki/Flip-flop_%28electronics%29
A | B | NOR
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
S | R | Q
0 | 0 | Maintain
0 | 1 | 0
1 | 0 | 1
1 | 1 | ???

## Slide 26: SR Flip-Flop / Latch
When S and R are zero, the latch maintains its value
When S=0 and R=1 the internal value becomes 0
When S=1 and R=0 the internal value becomes 0
Setting both to 1 means output is undefined
S | R | Q
0 | 0 | Maintain
0 | 1 | 0
1 | 0 | 1
1 | 1 | ???

## Slide 27: SR Flip-Flop / Latch
S | R | Q
0 | 0 | Maintain
0 | 1 | 0
1 | 0 | 1
1 | 1 | ???
Set / Reset
Stored Value

## Slide 28: My Simulators Can't Build an SR Latch :(
My Digital Logic Builder does not handle feedback loops so you can't build a SR latch from two NOR gates (unless I fix it)
SR Circuit Fails 
SR Component Works

## Slide 29: Gated D Latch
The Gated D Latch has a D (data) and a C (clock) inputs.
If C is zero, D is ignored, and the output is the most recent stored value
If C is 1, D is copied into the internal state
C | D | Q
0 | 0 | Maintain
0 | 1 | Maintain
1 | 0 | 0
1 | 1 | 1
C

## Slide 30: Gated D Latch
Store 1
Store 0
Ignore D
Ignore D
Clock to 0
Clock to 0

## Slide 31: Stack D Latches to Make a 3-bit Register

## Slide 32: Speed / Delay / Clocks
Latches and Flip-Flops

## Slide 33: Delay
The "longer" a circuit is, the longer it takes for the outputs to "settle" to their final values
Full Adder
Notes: This is a full adder laid out in the gates tool. It has three XOR gates and two AND gates. The point is that it has some “distance” from left to right - which translates to a slight delay form when the inputs are presented on the right to when you can reliably expect that the outputs are stable on the right outputs.

## Slide 34: Circuits can get quite long
CI
A
B
S
CO
CI
A
B
S
CO
CI
A
B
S
CO
CI
A
B
S
CO
4 bit adder
32 bit adder
64 bit adder?
64 bit multiplier?

## Slide 35
64 Bit
Adder
Once a circuit is designed and laid out, circuit simulators can compute the time it takes for signals to propagate through the circuit. We can not trust at the results to be accurate until sufficient time has passed.

## Slide 36: Clock Rate
Once we compute the delay of the slowest element of the Arithmetic and Logic parts of the CPU (aka the ALU), we can determine the number of times per second we can reliably do computations.

## Slide 37: What Determines Clock Rate?
The size of the chip (speed of light)
The number of transistors in the longest path within the ALU
The physical length of the longest path within the ALU (speed of light)
The speed at which each transistor switches between 0 and 1 (depends on the technology used to build the chip)
Chips are designed, redesigned, laid out, and simulated endlessly during development to produce the fastest clock rate

## Slide 38: Moore's Law
Moore's law is the observation that the number of transistors in an integrated circuit (IC) doubles about every two years.
X-Axis 1970 - 2020
Y-Axis 1000 - 50 billion
https://en.wikipedia.org/wiki/Moore%27s_law

## Slide 39: An Adder, Clock, and Register, Oh My!
The adder and its inputs is a "combinational circuit"
The latch is a "clocked circuit", ignoring its inputs while the clock is low, then "latching" the inputs in once the clock goes high
When the clock is low input changes are ignored

## Slide 40: An Adder, Clock, and Register, Oh My!
At this point, we have changed the adder input values.
The adder is adding the values and producing the sum reacting to whatever we do with a small delay.
The latch is ignoring all changes of the sum values

## Slide 41: An Adder, Clock, and Register, Oh My!
Once the clock is set to 1, the sum values are "latched" into the latch's internal memory.
At this point if we change inputs the latch may or may not get new sum values depending on the delay of the adder

## Slide 42: An Adder, Clock, and Register, Oh My!
So once we copy the sum inputs into the latch, the clock goes back down
We can once again change the adder inputs without affecting the latch since the clock is low.

## Slide 43: An Adder, Clock, and Register, Oh My!
As we change the inputs to the adder, its sum outputs change to 7 (with a short delay) but the latch retains its stored value of 6 since the clock is low.
If the clock goes high the 7 would be copied in as the new latch stored value

## Slide 44: For a good time…
Replace the clock button with an automatic 1 hertz clock (toggles once per second)
Play with the adder inputs and watch as the clock causes them to be copied into the latch.
See how many inputs you can change in one second
You can start and stop the clock by clicking on it 

## Slide 45: Counting using Gates

## Slide 46: Let's make a counter
If we take an adder, clock, and register, we can make a counting unit by adding 1 to the register each clock cycle.

## Slide 47: Let's make a counter
If we take an adder, clock, and register, we can make a counting unit by adding 1 to the register each clock cycle.
With the clock low and latch stored value of zero, the adder is continuously computing 0+1 but the latch is ignoring its inputs

## Slide 48: Let's make a counter
When the clock goes high, the latch stores its inputs, but does not copy the stored data to the latch output until the clock goes low
So, the adder is still computing 0+1 (i.e. not 1+1)

## Slide 49: Let's make a counter
When the clock goes low, the stored latch data is presented to the adder which computes 1+1=2 (after a short delay)

## Slide 50: Let's make a counter
If you keep toggling the clock the counter will count up to 7, overflow and restart the count at 0 again

## Slide 51: For a good time…
Replace the clock button with an automatic 1 hertz clock (toggles once per second)
You just made a simple seven-second clock!

## Slide 52: Programming with gates
Machine code programming in (0's and 1's)

## Slide 53
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 54: Inside a CPU
CPU
https://en.wikipedia.org/wiki/Central_processing_unit
Arithmetic / Logic Unit
Registers
Control Logic
Cache / Memory
Instructions
Data
Data
The ALU is circuits like adders
Registers are latches
Control logic and clock connect everything together
Instructions are taken from memory, decoded by the control logic which instructs the registers and ALU on what to do using wires, circuits and gates
Clock

## Slide 55: Foreshadowing..
Soon, we will design a simple CPU
  CDC 8512 – Inspired by the Control Data Corporation 6500
It will have a complete architecture
It will have a completely defined machine language
We will write real programs in CDC 8512 machine code and run them in an emulator
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 56: For now, we will build a simple CPU
One 3-bit latch
Two machine language instructions
  0 – Clear the latch
  1 – Add 1 to the latch
It will have a 1 Hz clock and be capable of executing one instruction per second
We will build this CPU and run it in our emulator

## Slide 57: Start with our counter
A latch feeds its stored value into one operand of an adder (clock low)
We hard-code the other adder input to be 1
We have a clock to tell the latch when to copy its new input to its internal state (clock high)

## Slide 58: Add control logic
Have an instruction input
  0 – Reset latch to zero
  1 – Copy output of adder
The instruction is fed into three AND gates
The sum values also go into the AND gates
The output of the AND gates goes into the Latch
Control
Logic

## Slide 59: Instruction 0
When instruction is zero, the output of the three AND gates is zero and the latch stays zero (reset)

## Slide 60: Instruction 1
When instruction is one, the sum values are passed to the latch inputs
And each clock rise/fall adds 1 to the latch value

## Slide 62: What is missing?
The instructions are not being read from memory.
It is like there is a switch on the front of the computer and it chooses between the two instructions
We want a flexible sequence of many instructions executed one after another (a.k.a. Software)

## Slide 63: Stored Sequences of Instructions

## Slide 64: Fetch-Decode-Execute-Cycle
CPU
ALU
Registers
Cache / Memory
Instructions
Data
Program Counter (PC) Register – Address of the next machine code instruction
Current Instruction Register (CIR)
The decoder looks at the bits of the CIR and using gates activates the correct ALU Element and register
The Clock tells the logic when to compute and when to copy results back to the register
PC
CIR
Decoder
https://en.wikipedia.org/wiki/Binary_decoder

## Slide 65: Machine Language Instructions
As part of the documentation for a CPU, we are given the bit patterns of the machine code for each of its instructions
There is usually a symbolic language that translates to machine language (assembler)
Assembly Language | Binary | Description
ZERO reg | 01000rrr | Set register to zero
CMPZ reg | 01001rrr | Compare register to zero
INC reg | 01010rrr | Increment register by 1
DEC reg | 01011rrr | Decrement register by 1

## Slide 66: Foreshadowing..
Soon, we will design a simple CPU
  CDC 8512 – Inspired by the Control Data Corporation 6500
It will have a complete architecture
It will have a completely defined machine language
We will write real programs in CDC 8512 machine code and run them in an emulator
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 67: Enough foreshadowing …

## Slide 68: Summary
In this lecture we started with simple gates like AND and OR
We built latches / registers for storage
We introduced the notion of a clock to wait until computation is complete
We talked about how clock rate has improved over time
We learned about the internals of a CPU – registers, arithmetic logic unit, program counter, and decoder logic
Up next: Designing and implementing a CPU architecture and its machine language

## Slide 69: Acknowledgements / Contributions
These slides are Copyright 2025- Charles R. Severance (online.dr-chuck.com) as part of www.ca4e.com and made available under a Creative Commons Attribution 4.0 License. Please maintain this last slide in all copies of the document to comply with the attribution requirements of the license. If you make a change, feel free to add your name and organization to the list of contributors on this page as you republish the materials.
Initial Development: Charles Severance, University of Michigan School of Information
Insert new Contributors and Translators here including names and dates
Continue new Contributors and Translators here