## Slide 1: The CDC 8512 Microprocessor
Dr. Charles R. Severance
online.dr-chuck.com

## Slide 2: Outline
Our two-instruction "CPU"
What is missing?
Why not study a real CPU?
The CDC8512 – inspired by the CDC 6500

## Slide 3
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Python for Everybody
Chapter 1
Slide 19

## Slide 4: CDC 8512 - Inspired by CDC 6500
Control Data Corporation
Mid 1960’s – mid-1970’s
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 5: CDC 8512 - Inspired by CDC 6500
Control Data Corporation
Mid 1960’s – mid-1970’s
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
  Pascal
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 6: About the CDC6500
60 bit words – Integer and floating point formats
6 bit characters - upper case only
Two kinds of data registers - A0-A7 – Address and X0-X7 Operands
To load from memory you put the address in A1-A5 and the data from memory is loaded into the corresponding X1-X5
To store into memory you put the data in X6 or X7 and Set the corresponding A6 or A7 to the location where you want the memory stored

## Slide 7
http://ygdes.com/CDC/60100000D_6600refMan_Feb67.pdf
To provide a more compact symbolic language, the 24 operating registers are identified by letters and numbers:
A = Address Register (A0, A1 .. A7)
B = increment register (B0, B1 … B7)
X = operand register (X0, X1 … X7)
The operand registers hold operands and results for servicing the functional units. Five registers (X1-X5) hold read operands from Central Memory and two registers X6 – X7) hold results to be sent to Central Memory (Figure 3-2).
Operands and results transfer between memory and these registers as a result of placing a quantity into a corresponding address register (A1-A7).
-- Control Data 6400/6500/6660 Computer Systems Reference Manual
Figure 3.2

## Slide 8: About the CDC8512
8 bit words – Positive integers only (i.e. like a C char)
8 bit characters – ASCII (i.e. like a C char)
256 bytes of Instruction memory and 256 bytes of Data memory
Eight 8-bit registers (A0-A3) and (X0-X3)
When A0 is set it causes a load from Data[A0] into X0 to happen
When A1 is set it causes a load from Data[A1] into X1 to happen
When A2 is set it causes a store from X2 into Data[A2] to happen
When A3 is set it causes a store from X3 into Data[A3] to happen

## Slide 9: CDC8512 Architecture
255
A0
255
X0
255
A1
255
X1
255
A2
255
X2
255
A3
255
X3
255
PC
<=>
CM
255
0x00
255
0x01
255
0x02
255
0x03
255
0x04
255
0x05
…
255
0xFD
255
0xFE
255
0xFF
Central Processing Unit
Instruction Memory
255
0x00
255
0x01
255
0x02
255
0x03
255
0x04
255
0x05
…
255
0xFD
255
0xFE
255
0xFF
Data Memory
Load
Registers
Store
Registers

## Slide 10: CDC 8512 – Instruction Set

## Slide 11: Set a Register
SX3 'C' # Set X3 to the value for ASCII C (67)
SA3 0 # Set A3 to zero and store 'C' in data memory location 0x00
SA1 0 # Set A1 to zero and load memory location 0x00 into X0
SX3 X1 # Copy X3 to X1
SA3 0x01 # Set A3 to 1 and store 'C' in data memory location 0x01
SX3 0x00 # Set X3 to zero
SA3 0x02 # Set A3 to 0x02 and store X3 into location 0x02
# Note constants can be decimal (0-255) hexadecimal (0x00-0xff) or a single
# ASCII character in single quotes 'a'

## Slide 12: Register Arithmetic
SX3 'H' # Set X3 to the value for ASCII H
SA3 0 # Set A3 to zero and store 'H' in data memory location 0x00
SX3 'e' # Set X3 to 'e'
INC A3 # Add 1 to A3 and store 'e' in location 0x01
SX3 'l' # Set X3 to 'l'
ADD A3, 1 # Add 1 to A3 and store 'l' in location 0x01
INC A3 # Add 1 to A3 and store 'l' in location 0x02
ADD X3, 4 # Add 3 to X3 so that it is now 'p'
DEC X3 # Subtract 1 from X3 so that it is now 'o'
INC A3 # Add 1 to A3 and store '0' in location 0x03
SX3 0 # Set X3 to integer zero
INC A3 # Add 1 to A3 and store integer 0 in location 0x04
PS 0 # Print memory starting at data address 0 as an
# ASCII string, stopping when a zero is encountered
#
# This will print: Hello

## Slide 13: Comparison and Jumps
JP 0x12 # Set the PC (Program Counter) to an instruction address and
# continue execution at that address
CMP X3, 42 # Compare a register to a constant and set comparison status
JE 0x12 # Jump to the instruction address if comparison status is =
JG 0x12 # Jump to the instruction address if comparison status is >
JL 0x12 # Jump to the instruction address if comparison status is <

## Slide 14: Miscellaneous Instructions
PS # Print data area starting at specified data address
# stopping when an integer 0 byte is encountered
DI # Dump Instruction area in hex 16 bytes per line
# stop after two successive zeros are encountered in an output line
DD # Dump Data area in hex 16 bytes per line
# stop after two successive zeros are encountered in an output line
HALT # Stop Execution

## Slide 15: Summary
SX3 A3 # Copy a register to another
SX3 42 # Set a register to an 8-bit
INC A1 # Add 1 to a register
DEC X3 # Subtract 1 from a register
ADD X1, 42 # Add a constant to a register
SUB X3, 42 # Subtract a constant from a register
JP 0x12 # Jump to a label
CMP X3, 42 # Compare a register to a constant and set comparison status
JE 0x12 # Jump to the label if CMP was equal
JG 0x12 # Jump to the label if CMP was >
JL 0x12 # Jump to the label if CMP was <
PS # Print data area as character string
DI # Dump Instruction area in hex 16 per line
DD # Dump data area in hex 16 per
HALT # Stop Execution

## Slide 16: CDC 8512 – Machine Language
(a.k.a. the zeros and ones of programming)

## Slide 17: Halt Instruction
0
0
0
0
0
0
0
0
HALT # Stop the CPU

## Slide 18: Single Register 8-bit Instruction
0
1
0
0
1
0
1
0
INC A2 # Add 1 to A2
Register
Number
0 = A register
1 = X register
Register
Increment Register

## Slide 19: Single Register 8-Bit Instruction
0
1
0
1
0
1
1
0
DEC X2 # Decrement X2
Register
Number
0 = A register
1 = X register
Register
Decrement Register

## Slide 20: Set Register to Constant (2 byte instruction)
1
0
0
0
1
1
0
0
SX0 0x43 # Set X0
SX0 67 # Set X0
SX0 'C' # Set X0
Register
Number
0 = A register
1 = X register
0x43

## Slide 21: Two Register Instruction
1
1
0
0
1
1
1
1
SX3 A1 # Copy A1 to X3
Register
Number
0 = A register
1 = X register
Register
Number
0 = A register
1 = X register
Source
Register
Destination
Register
Register
Copy