## Slide 1: The CDC 6504 Microprocessor
Dr. Charles R. Severance
online.dr-chuck.com

## Slide 2: Outline
Our two-instruction "CPU" - What is missing?
Instruction decoding and control
Real CPUs – Intel x86, ARM, 6502 and Intel 4004
The CDC6504 – inspired by the CDC 6500
  Architecture
  Machine Language
  Assembly Language
Emulators – JavaScript – Old video Games at archive.org
Reading on CPUs

## Slide 3: Review: What is missing?
The instructions are not being read from memory.
It is like there is a switch on the front of the computer and it chooses between the two instructions
We want a flexible sequence of many combinations of instruction sequences(a.k.a. Software)

## Slide 4
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Python for Everybody
Chapter 1
Slide 19
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 5: Fetch-Decode-Execute-Cycle
CPU
ALU
Registers
Cache / Memory
Instructions
Data
Program Counter (PC) Register – Address of the next machine code instruction
Current Instruction Register (CIR)
The decoder looks at the bits of the CIR and using gates activates the correct ALU Element and register
The Clock causes the logic when to compute and when to copy results back to the register
PC
CIR
Decoder
https://en.wikipedia.org/wiki/Binary_decoder

## Slide 6: Machine Language Instructions
As part of the documentation for a CPU, we are given the bit patterns of the machine code for each of its instructions
There is usually a symbolic language that translates to machine language (assembler)
Assembly | Opcode | Description
CLR X | 00010010 | Clear X register (X = 0).
INX | 11101000 | Increment X register by 1
LDX #value | 10100010 | Load X register with immediate (constant) value
LDX $address | 10100110 | Load X register from zero-page memory address
STX $address | 10000110 | Store X register to zero-page memory address

## Slide 7: Let's learn Base-16 (Hexadecimal)
Base 16 is easy to convert to bits and much less verbose than Base-2

## Slide 8: Recall Base-2
Base–2 to Base-10 for numbers less than 8
A.k.a. 3-bit numbers
Base-10 | Base-2
0 | 0
1 | 1
2 | 10
3 | 11
4 | 100
5 | 101
6 | 110
7 | 111
1 1 0 = 6
4s 2s 1s

## Slide 9: The first problem with Base-16
We only have 0-9 and we need to be able to represent 0-15 in a single base-16 digit
Thankfully we have emoji's
  10 ✊
  11 ☝️
  12 ✌️
  13 🤟 (also Rock on!)
  14 🍀
  15 🖐
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | ✊
11 | 1011 | ☝️
12 | 1100 | ✌️
13 | 1101 | 🤟
14 | 1110 | 🍀
15 | 1111 | 🖐

## Slide 10: AI suggested these emoji's
AI suggested emoji's
  10 🔟
  11 ⏸️
  12 🕛
  13 🕐 (1PM is 1300 hours)
  14 🕑 (2PM is 1400 hours)
  15 🕒 (3 PM is 1500 hours)
American Sign Language(ASL) uses one hand but requires motion
British Sign Language is different
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | 🔟
11 | 1011 | ⏸️
12 | 1100 | 🕛
13 | 1101 | 🕛
14 | 1110 | 🕑
15 | 1111 | 🕒

## Slide 11: No emojis in 1940 😭📅😭
We only have 0-9 as numbers and we need to be able to represent 0-15 in a single base-16 digit
So we used A-F to represent 10-15 for base-16 numbers
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 12: Base-10 and Base-16 (Hexadecimal) numbers
Need a cheat sheet
Base-10
12310 = 1 x 102 + 2 x 101 + 3 * 100
= 1 x 100 + 2 * 10 + 3 * 1 = 12310
Base-16
7B16 = 7 * 161 + 11 * 160 =
= 112 + 11 = 12310
Base-10 | Base-16
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F

## Slide 13: Base-16 to/from Base-2
Since 2 and 16 are even powers of 2, each Base-16 represents exactly four base-2 digits so we can convert digit by digit
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F
7B 16
0111 1011 2
A2 16
1010 0010 2
Hex is just more succinct Base-2

## Slide 14: Keep it simple for now
Go through base-10 if it helps
1 0 1 0 = 1010 = A16
1 0 0 0 = 810 = 816
1 1 1 1 = 1510 = F16
8s 4s 2s 1s
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 15: Chuck's not-so-quick Guide to Base-16
F16 = 1510 = 11112 (Easy one less than 16)
E16 = 1410 = 11102 (one less than 15)
A16 = 1010 = 10102 (8+2)
B16 = 1110 = 10102 (8+2+1)
C16 = 😕 🧠 🤟 = 8+3 = 10112
D16 = 😕 🤔 ⬆️ ⬇️ 🧠 📝 😠
AI: What is a good way to be able to do hex to base 2 conversions in your head?

## Slide 16: ASCII – 8 Bits
https://en.wikipedia.org/wiki/ASCII
http://www.catonmat.net/download/ascii-cheat-sheet.png
https://www.ca4e.com/tools/ascii/
ASCII Characters are 8-bits and can be nicely represented with two hex digits (a.k.a. nibbles)
American Standard Code for Information Interchange

## Slide 17
http://unicode.org/charts/

## Slide 18: Multi-Byte Characters (a quick aside…)
To represent the wide range of characters computers must handle we represent characters with more than one byte
  UTF-16 – Fixed length - Two bytes
  UTF-32 – Fixed Length - Four Bytes
  UTF-8 – 1-4 bytes
    - Upwards compatible with ASCII
    - Automatic detection between ASCII and UTF-8
    - UTF-8 is recommended practice for encoding data to be exchanged between systems
https://en.wikipedia.org/wiki/UTF-8

## Slide 19: The Essense of Programming
Hint: Machine code will both be simpler but a lot more complex. There is a reason we built languages like C and Python.

## Slide 20: What is Programming? Python for Everybody
www.py4e.com

## Slide 21
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Python for Everybody
Chapter 1
Slide 19
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 22: Program Steps or Program Flow
Like a recipe or installation instructions, a program is a sequence of steps to be done in order.
Some steps are conditional - they may be skipped.
Sometimes a step or group of steps is to be repeated.
Sometimes we store a set of steps to be used over and over as needed several places throughout the program

## Slide 23: Sequential Steps
Program:
x = 2
print(x)
x = x + 2
print(x)
Output:
2
4
x = 2
print(x)
x = x + 2
print(x)
When a program is running, it flows from one step to the next. As programmers, we set up “paths” for the program to follow.

## Slide 24: Conditional Steps
Output:
Smaller
Finis
Program:
x = 5
if x < 10:
print('Smaller')
if x > 20:
print('Bigger')
print('Finis')
x = 5
x < 10 ?
print('Smaller')
x > 20 ?
print('Bigger')
print('Finis')
Yes
No
No
Yes

## Slide 25: Repeated Steps
Output:
5
4
3
2
1
Blastoff!
Program:
n = 5
while n > 0 :
print(n)
n = n – 1
print('Blastoff!')
n > 0 ?
Loops (repeated steps) have iteration variables that change each time through a loop.
No
print('Blastoff')
Yes
n = 5
print(n)
n = n -1

## Slide 26: Variables
A variable is a named place in the memory where a programmer can store data and later retrieve the data using the variable “name”
Programmers get to choose the names of the variables
You can change the contents of a variable in a later statement
12.2
x
14
y
100
x = 12.2
y = 14
x = 100

## Slide 27: The True Story of Python Assignment Statements
Charles Severance
www.dj4e.com

## Slide 28: What *IS* a Python variable?
A Python variable is a symbolic name that is a pointer or reference to an object.
We can examine what a variable is ”pointing to” using the id() function in Python
https://realpython.com/python-variables/#object-references
>>> x = 42
>>> y = x
>>> print(id(x))
4311543376
>>> print(id(y))
4311543376
int
42
x
y
Object

## Slide 29: From Python to C (Rosetta Stone) www.cc4e.com

## Slide 30: Counted Loop
for i in range(5) :
print(i)
#include <stdio.h>
int main() {
int i;
for(i=0; i<5; i++) {
printf("%d\n",i);
}
}
0
1
2
3
4
cc_02_07.c

## Slide 31: Read A File
hand = open('romeo.txt')
for line in hand:
print(line.strip())
#include <stdio.h>
int main() {
char line[1000];
FILE *hand;
hand = fopen("romeo.txt", "r");
while( fgets(line, 1000, hand) != NULL ) {
printf("%s", line);
}
}
But soft what light through yonder window breaks
It is the east and Juliet is the sun
Arise fair sun and kill the envious moon
Who is already sick and pale with grief
cc_02_06.c

## Slide 32: Shouting
hand = open('romeo.txt')
for line in hand:
print(line.strip().upper())
#include <stdio.h>
#include <string.h>
#include <ctype.h>
int main() {
char line[1000];
FILE *hand;
int i;
hand = fopen("romeo.txt", "r");
while( fgets(line, 1000, hand) != NULL )
for(i=0; i<strlen(line); i++)
putchar(toupper(line[i]));
}
BUT SOFT WHAT LIGHT THROUGH YONDER WINDOW BREAKS
IT IS THE EAST AND JULIET IS THE SUN
ARISE FAIR SUN AND KILL THE ENVIOUS MOON
WHO IS ALREADY SICK AND PALE WITH GRIEF
cc_02_11.c

## Slide 33: Summary of Basics of Programming
Patterns
  Sequential
  Conditional
  Repeated
Variables
  In Python and Java "point" to objects, that are created, reused, and garbage collected
  In C and Machine Language, variables are *places* (i.e. like a little drawer with an address / label)

## Slide 34: Lets Design a CPU
The CDC6504 is designed to be understandable

## Slide 35: Why wouldn't we use a modern CPU?
Intel X86 – Introduced in 1978
  Focused on Desktop computers
  Includes AMD
ARM – Introduced in 1985
  Focused on early cell phones
  Core Instruction Set + Extensions
Real CPUs are quite intricate because over time they added new instructions and kept the old ones for compatibility.

## Slide 36: ARM Assembly
.global _start
_start:
MOV R0, #3 @ Load 3 into R0
MOV R1, #4 @ Load 4 into R1
ADD R0, R0, R1 @ R0 = R0 + R1 (3 + 4 = 7)
MOV R7, #1 @ syscall: exit
SWI 0 @ exit with code in R0 (7)

## Slide 37: Intel X86 Assembly
global _start
_start:
mov eax, 3 ; Load 3 into eax
mov ebx, 4 ; Load 4 into ebx
add eax, ebx ; eax = eax + ebx (3 + 4 = 7)
mov ebx, eax ; exit code = sum (7)
mov eax, 1 ; syscall number for exit
int 0x80 ; make syscall

## Slide 38: MOS Technology 6502
Launched in 1975 and cost $25
4,528 NMOS Transistors
https://en.wikipedia.org/wiki/MOS_Technology_6502
Apple I, Apple II, Commodore PET, Commodore VIC-20, Commodore 64 (6510), Atari 2600, Atari 400, Atari 800, Atari XL series, Atari XE series, BBC Micro, Acorn Atom, Acorn Electron, Nintendo NES (2A03), Oric-1, Oric Atmos, Philips P2000, Ohio Scientific Challenger 1P, KIM-1 …

## Slide 39: CDC 6504 – Named for the CDC 6500
Control Data Corporation
Mid 1960’s – mid-1970’s
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 40: CDC 6504 – Named for CDC 6500
Control Data Corporation
Mid 1960’s – mid-1970’s
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
  Pascal
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 41: The CDC6504 Architecture

## Slide 42: CDC6504 Architecture
0x00
A0
0x00
PC
<=>
CMP
01000110
0x00
01010110
0x01
01010110
0x02
01000010
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Data Memory
PC – Program Counter
CMP – Result of most recent comparison
Mode – Error indicator
A and X registers shown in hex
Instruction memory shows in base-2 for easy decoding
Data memory shows in hex – will usually contain ASCII
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3
What
Next?

## Slide 43: Memory Architecture
0x00
A0
0x00
PC
<=>
CMP
01000110
0x00
01010110
0x01
01010110
0x02
01000010
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
X0 / X1 are Load Registers
X2 / X3 are Store Registers
Setting A0 / A1 causes a load into X0 / X1
Setting A2 / A3 causes a store from X2 / X3
Data memory (255) holds values when we don't have enough registers
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3

## Slide 44: Programming the CDC6504
Assembly language is easier to read and translates directly to binary machine language
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Binary | Description
ZERO reg | 01000rrr | Set register to zero
CMPZ reg | 01001rrr | Compare register to zero, set CMP flag
INC reg | 01010rrr | Increment register by 1
DEC reg | 01011rrr | Decrement register by 1
rrr | Register
000 | A0
001 | A1
010 | A2
011 | A3
100 | X0
101 | X1
110 | X2
111 | X3

## Slide 45: Our first Program
0x00
A0
0x00
PC
<=>
CMP
01000110
0x00
01010110
0x01
01010110
0x02
01000010
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
A program
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3
0x00
0x06
00000000
0x06
ZERO X2
INCR X2
INCR X2
Zero A2 (stores X2 in memory 0x00)
Halt

## Slide 46: Our first Program
0x00
A0
0x00
PC
<=>
CMP
01000110
0x00
01010110
0x01
01010110
0x02
01000010
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
A program
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3
0x00
0x06
00000000
0x06
ZERO X2
INCR X2
INCR X2
Zero A2 (stores X2 in memory 0x00)
Halt

## Slide 47: Our first Program
0x00
A0
0x01
PC
<=>
CMP
01000110
0x00
01010110
0x01
01010110
0x02
01000010
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
A program
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x01
X2
0x00
X3
0x00
0x06
00000000
0x06
ZERO X2
INCR X2
INCR X2
Zero A2 (stores X2 in memory 0x00)
Halt

## Slide 48: Our first Program
0x00
A0
0x02
PC
<=>
CMP
01000110
0x00
01010110
0x01
01010110
0x02
01000010
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
A program
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x02
X2
0x00
X3
0x00
0x06
00000000
0x06
ZERO X2
INCR X2
INCR X2
Zero A2 (stores X2 in memory 0x00)
Halt

## Slide 49: Our first Program
0x00
A0
0x03
PC
<=>
CMP
01000110
0x00
01010110
0x01
01010110
0x02
01000010
0x03
00000000
0x04
00000000
0x05
0x02
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
A program
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x02
X2
0x00
X3
0x00
0x06
00000000
0x06
ZERO X2
INCR X2
INCR X2
Zero A2 (stores X2 in memory 0x00)
Halt

## Slide 50: Our CPU from Logic, Gates, Transistors
There is a lot of overlap between the CDC6504 and our two instruction CPU….

## Slide 51: Our CPU from Logic, Gates, Transistors
Our CPU implements two instructions
  Zero Register
  Increment Register
There is no program counter because there is no instruction memory
But….
Increment
Register
Instruction
Decode
Logic

## Slide 52: Looking closer
The difference between the ZERO and INCR instructions is one bit
If bit 5 is a zero, the register is zeroed
If bit five is a one, the register is incremented
01000110
0x00
01010110
0x01
ZERO X2
INCR X2

## Slide 53: If you had time…
With what you know and and better design tools you could design a CDC6504
  Logic
  Memory
  VLSI layout
  Manufacture
It would probably be about as complex as the Intel 4004
The Intel 4004 is a better design 

## Slide 54: CDC6504 Machine Language
https://www.ca4e.com/cdc6504/documentation.html

## Slide 55: 8-Bit Instructions (review)
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Binary | Description
ZERO reg | 01000rrr | Set register to zero
CMPZ reg | 01001rrr | Compare register to zero, set CMP flag
INC reg | 01010rrr | Increment register by 1
DEC reg | 01011rrr | Decrement register by 1
rrr | Register
000 | A0
001 | A1
010 | A2
011 | A3
100 | X0
101 | X1
110 | X2
111 | X3
01000110
0x00
01010110
0x01
ZERO X2
INCR X2

## Slide 56: 16-Bit Instructions (a.k.a. immediate)
Immediate values are like constants
The byte immediately following the instruction is the constant value
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Binary | Description
SET reg, value | 10000rrr + value | Set register to immediate value (0-255, 0x00-0xFF, or 'A')
ADD reg, value | 10010rrr + value | Add immediate value to register (0-255, 0x00-0xFF, or 'A')
SUB reg, value | 10011rrr + value | Subtract immediate value from register (0-255, 0x00-0xFF, or 'A')
10000101
0x00
00101010
0x01
Set X1, 42
(the 42)

## Slide 57: There is no IF statement in Machine Code
To do conditional execution we use a compare instruction which sets a comparison flag (CMP)
Then in the following instruction we do a conditional jump to an address in instruction memory based on the latest comparison result
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Binary | Description
CMP reg, value | 10001rrr + value | Compare register to immediate value (0-255, 0x00-0xFF, or 'A')
JE label/value | 10100000 + address | Jump if CMP == "="
JL label/value | 10100001 + address | Jump if CMP == "<"
JG label/value | 10100010 + address | Jump if CMP == ">"
JP label/value | 10100011 + address | Unconditional jump

## Slide 58
Assembly | Binary | Description
CMP reg, value | 10001rrr + value | Compare register to immediate value (0-255, 0x00-0xFF, or 'A')
JE label/value | 10100000 + address | Jump if CMP == "="
JL label/value | 10100001 + address | Jump if CMP == "<"
JG label/value | 10100010 + address | Jump if CMP == ">"
JP label/value | 10100011 + address | Unconditional jump
10000110
0x00
01110000
0x01
Set X2, 'p'
(the 'p')
10001110
0x02
01100001
0x03
CMP X2, 'a'
(the 'a')
10100001
0x04
00101010
0x05
JL 0x08
The 0x08)
10000101
0x06
00101010
0x07
SUB X2, 0x20
(the 0x20)
00000000
0x08
Halt (X2 is 'P')
Notes: This is a simple program to check if a character ('p') is already upper case. If it is not upper case, we add 0x20 to the ASCII value to convert it to upper case. At the end of the program, X2 contains the upper-case value whether the initial value was an upper- or lower-case letter. The result in X2 is 'P' (upper-case)

## Slide 59
10000110
0x00
01110000
0x01
Set X2, 'p'
(the 'p')
10001110
0x02
01100001
0x03
CMP X2, 'a'
(the 'a')
10100001
0x04
00101010
0x05
JL 0x08
(The 0x08)
10000101
0x06
00101010
0x07
SUB X2, 0x20
(the 0x20)
00000000
0x08
Halt (X2 is 'P')
X2 = 'p'
Yes
X2 ? 'a'
CMP < ?
X2 = X2 – 0x20
Halt
No
Notes: This is a simple program to check if a character ('p') is already upper case. If it is not upper case, we subtract 0x20 to the ASCII value to convert it to upper case. At the end of the program, X2 contains the upper-case value whether the initial value was an upper- or lower-case letter. The result in X2 is 'P' (upper-case)

## Slide 60: Assembly gives us labels
No need to compute addresses by hand
SET X2, 'p'
CMP X2, 'a'
JL skip
SUB X2, 0x20
skip:
HALT
10000110
0x00
01110000
0x01
Set X2, 'p'
(the 'p')
10001110
0x02
01100001
0x03
CMP X2, 'a'
(the 'a')
10100001
0x04
00101010
0x05
JL 0x08
(The 0x08)
10000101
0x06
00101010
0x07
SUB X2, 0x20
(the 0x20)
00000000
0x08
Halt (X2 is 'P')

## Slide 61: Jumps are far simpler than "if logic"
You can think of the unconditional Jump as a SET into the Program Counter (PC) register
A conditional jump is a conditional set of the PC register
Assembly | Binary | Description
CMP reg, value | 10001rrr + value | Compare register to immediate value (0-255, 0x00-0xFF, or 'A')
JE label/value | 10100000 + address | Jump if CMP == "="
JL label/value | 10100001 + address | Jump if CMP == "<"
JG label/value | 10100010 + address | Jump if CMP == ">"
JP label/value | 10100011 + address | Unconditional jump

## Slide 62: There is no "for" or "while" in machine language
ZERO X0
loop:
CMP X0, 5
JE end
INC X0
JP loop
end:
HALT
X0 = 0
Yes
X2 ? 5
CMP = ?
JP loop
Halt
No
X0 = X0 + 1

## Slide 63
Assembly | Binary | Description
HALT | 00000000 | Stop program execution
ZERO reg | 01000rrr | Set register to zero
CMPZ reg | 01001rrr | Compare register to zero, set CMP flag
INC reg | 01010rrr | Increment register by 1
SET reg, value | 10000rrr + value | Set register to immediate value (0-255, 0x00-0xFF, or 'A')
CMP reg, value | 10001rrr + value | Compare register to immediate value (0-255, 0x00-0xFF, or 'A')
ADD reg, value | 10010rrr + value | Add immediate value to register (0-255, 0x00-0xFF, or 'A')
SUB reg, value | 10011rrr + value | Subtract immediate value from register (0-255, 0x00-0xFF, or 'A')
JE label/value | 10100000 + address | Jump if CMP == "="
JL label/value | 10100001 + address | Jump if CMP == "<"
JG label/value | 10100010 + address | Jump if CMP == ">"
MOV dest, src | 11dddsss | Copy source register to destination register
https://www.ca4e.com/tools/cdc6504/documentation.html

## Slide 64: CDC 6504 – Assembly Language
https://www.ca4e.com/cdc6504/documentation.html

## Slide 65: Set a Register
SET X3, 'C' ; Set X3 to the value for ASCII C (67)
SET A3, 0 ; Set A3 to zero and store 'C' in data memory location 0x00
SET A1, 0 ; Set A1 to zero and load memory location 0x00 into X0
MOV X1, X3 ; Copy X3 to X1
SET A3, 0x01 ; Set A3 to 1 and store 'C' in data memory location 0x01
SET X3, 0x00 ; Set X3 to zero
SET A3, 0x02 ; Set A3 to 0x02 and store X3 into location 0x02
; Note constants can be decimal (0-255) hexadecimal (0x00-0xff) or a single
; ASCII character in single quotes 'a'

## Slide 66: Register Arithmetic
; This will print: Hello
SET X3, 'H' ; Set X3 to the value for ASCII H
SET A3, 0 ; Set A3 to zero and store 'H' in data memory location 0x00
SET X3, 'e' ; Set X3 to 'e'
INC A3 ; Add 1 to A3 and store 'e' in location 0x01
SET X3, 'l' ; Set X3 to 'l'
ADD A3, 1 ; Add 1 to A3 and store 'l' in location 0x02
INC A3 ; Add 1 to A3 and store 'l' in location 0x03
ADD X3, 4 ; Add 4 to X3 so that it is now 'p'
DEC X3 ; Subtract 1 from X3 so that it is now 'o'
INC A3 ; Add 1 to A3 and store '0' in location 0x04
SET X3, 0 ; Set X3 to integer zero
INC A3 ; Add 1 to A3 and store integer 0 in location 0x05
HALT ; Print memory starting at data address 0 as an
; ASCII string, stopping when a zero is encountered

## Slide 67: Comparison and Jumps
JP 0x12 ; Set the PC (Program Counter) to an instruction address and
; continue execution at that address
CMP X3, 42 ; Compare a register to a constant and set comparison status
JE 0x12 ; Jump to the instruction address if comparison status is =
JG 0x12 ; Jump to the instruction address if comparison status is >
JL 0x12 ; Jump to the instruction address if comparison status is <

## Slide 68: Miscellaneous Instructions
HALT # Stop Execution

## Slide 69: Data Directive – Assembly Only
Assembly | Description
DATA 'string' | Pre-populates data memory (not instruction memory) with a null-terminated string. Data is loaded starting at memory address 0.
DATA 0x00 0x0A ... | Pre-populates data memory (not instruction memory) with a space-separated list of hexadecimal values. Data is loaded starting at memory address 0.

## Slide 70: Summary
MOV X3, A3 ; Copy a register to another
SET X3, 42 ; Set a register to an 8-bit value
INC A1 ; Add 1 to a register
DEC X3 ; Subtract 1 from a register
ADD X1, 42 ; Add a constant to a register
SUB X3, 42 ; Subtract a constant from a register
JP lab ; Jump to a label
CMP X3, 42 ; Compare a register to a constant and set comparison status
JE 0x12 ; Jump to the address if CMP was equal
JG 0x12 ; Jump to the address if CMP was >
JL 0x12 ; Jump to the address if CMP was <
lab:
HALT ; Stop Execution
DATA 'Hello world'

## Slide 71: CDC 6504 – Decoding Machine Language
(a.k.a. the zeros and ones of programming)

## Slide 72: CDC 6504 - Assembly / Machine Code
SET X2, 'H'
ZERO A2
SET X2, 'i'
INC A2
PS
HALT
10000110
01001000 'H'
01000010
10000110
01101001 'i'
01010010
00000001
00000000

## Slide 73: Single Register 8-bit Instruction
0
1
0
0
0
0
1
0
ZERO A2
Register
Number
0 = A register
1 = X register
Register
Zero Register
Op Code

## Slide 74: Set Register to Constant (16-bit instruction)
1
0
0
0
0
1
1
0
SET X2,'H'
Register
Number
0 = A register
1 = X register
0
1
0
0
1
0
0
0
ASCII for 'H'
Set Register
Op Code

## Slide 75: Single Register 8-Bit Instruction
0
1
0
1
0
0
1
0
INC A2 # Increment A2
Register
Number
0 = A register
1 = X register
Register
Decrement Register
Op Code

## Slide 76: Two Register Instruction
1
1
0
0
1
1
1
1
MV A1,X3 ; Copy A1 to X3
Register
Number
0 = A register
1 = X register
Register
Number
0 = A register
1 = X register
Destination
Register
Source
Register
Register
Copy

## Slide 77: Halt Instruction
0
0
0
0
0
0
0
0
HALT # Stop the CPU

## Slide 78: CDC6504 Emulator in JavaScript
// 5-bit patterns (bits 7-3)
else if ((instruction >> 3) === 0x08) { // 01000xxx - ZERO
const register = instruction & 0x07;
const regName = this.getRegisterName(register);
this.cpu[regName] = 0;
// CDC 6500 load/store architecture:
if (regName === 'a0') {
this.cpu.x0 = this.cpu.memory[this.cpu.a0];
} else if (regName === 'a1') {
this.cpu.x1 = this.cpu.memory[this.cpu.a1];
} else if (regName === 'a2') {
this.cpu.memory[this.cpu.a2] = this.cpu.x2;
} else if (regName === 'a3') {
this.cpu.memory[this.cpu.a3] = this.cpu.x3;
}
pcIncrement = 1;
}

## Slide 79: Emulators for Fun

## Slide 80: Building Emulators for Historical CPUs
It is not all that difficult to build an emulator for an older (simpler) CPU
Modern processors on our phones and computers are so fast that JavaScript in a browser can emulate historical machine code faster than the original hardware
The computer / phone / browser graphics are also far better
And it can be great fun

## Slide 81: Archive.org: Internet Arcade

## Slide 82: Game: Dig Dug

## Slide 83: Dig Dug Startup – JSMAME Emulator

## Slide 84: CPU Evolution
Why we invented our own super simple processor to learn.

## Slide 85: Apple Computer Processors over time
MOS 6502 - Apple II – 1977 - 1993
Motorola MC68000 – Macintosh 1984-1994
IBM PowerPC – Macintosh 1994 – 2006
Intel x86 – Macintosh (2006-2020)
Samsung ARM – iPhone (2007-2009)
Apple ARM – iPhone (2010-Present)
Apple ARM – Macintosh (2020-Present)
Apple currently redesigns their CPUs based on workload over time – Image Processing / Audio / Video / Gaming / Artificial Intelligence

## Slide 86: Reading: Post-Risc Architecture
https://cse.msu.edu/~enbody/postrisc/postrisc2.htm

## Slide 87: Reading: Intel 4004
https://www.4004.com/
http://e4004.szyc.org/
http://e4004.szyc.org/iset.html
http://e4004.szyc.org/emu/

## Slide 88: http://e4004.szyc.org/iset.html

## Slide 89: http://e4004.szyc.org/emu/

## Slide 90: WASM – Web Assembly
There is a machine language emulator built into browsers called Web Assembly
For a wide range of software, compiling to WASM and running in JavaScript is enough
WASM is a different syntax than most Assembly languages – but it still compiles to a binary-machine code
C Programming for Everybody (www.cc4e.com) C Playground compiles C to WASM and then runs the WASM in the user's browser

## Slide 91: WASM Hello World
;; Hello World WASM Example
(module
(import "console" "log" (func $log (param i32 i32)))
(memory 1)
(data (i32.const 0) "Hello, World!")
(func $main (result i32)
(call $log (i32.const 0) (i32.const 13))
(i32.const 42)
)
(export "main" (func $main))
)
00000000: 00 61 73 6d 01 00 00 00 01 0a 02 60 02 7f 7f 00 |.asm.......`....|
00000010: 60 00 01 7f 02 0f 01 07 63 6f 6e 73 6f 6c 65 03 |`.......console.|
00000020: 6c 6f 67 00 00 03 02 01 01 05 03 01 00 01 07 11 |log.............|
00000030: 02 06 6d 65 6d 6f 72 79 02 00 04 6d 61 69 6e 00 |..memory...main.|
00000040: 01 0a 0c 01 0a 00 41 00 41 0d 10 00 41 2a 0b 0b |......A.A...A*..|
00000050: 13 01 00 41 00 0b 0d 48 65 6c 6c 6f 2c 20 57 6f |...A...Hello, Wo|
00000060: 72 6c 64 21 |rld!|

## Slide 93: Summary
Fetch-Decode-Execute (a.k.a. Fetch-Execute-Cycle)
Look at the Intel x86 and ARM processor families
Explored the CDC6504 architecture, instruction set, assembly and machine languages
Explored an increasing use of in-browser emulators for games and other applications
Looked at CPU Evolution over time
Looked back at the Intel 4004
Looked forward at Web Assembly (WASM)

## Slide 94: Acknowledgements / Contributions
These slides are Copyright 2025- Charles R. Severance (online.dr-chuck.com) as part of www.ca4e.com and made available under a Creative Commons Attribution 4.0 License. Please maintain this last slide in all copies of the document to comply with the attribution requirements of the license. If you make a change, feel free to add your name and organization to the list of contributors on this page as you republish the materials.
Initial Development: Charles Severance, University of Michigan School of Information
Insert new Contributors and Translators here including names and dates
Continue new Contributors and Translators here