## Slide 1: The CDC 6504 Microprocessor
Dr. Charles R. Severance
online.dr-chuck.com

## Slide 2: Outline
Start from our "two instruction CPU" from the previous section
Hexadecimal Notation
Review: What is Programming from PY4E
Real CPUs – Intel x86, ARM, and MOS 6502
The CDC6504 – Mostly 6502 with homage to CDC 6500
  Architecture
  Machine Language
  Assembly Language
Real CPU Emulators – JavaScript / WASM – Old video Games
CPU Evolution from over the decades

## Slide 3: Review: What is missing?
The instructions are not being read from memory.
It is like there is a switch on the front of the computer and it chooses between the two instructions
We want a flexible sequence of many combinations of instruction sequences(a.k.a. Software)

## Slide 4
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
11100010
11101000
Python for Everybody
Chapter 1
Slide 19
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 5: Fetch-Decode-Execute-Cycle
CPU
ALU
Registers
Cache / Memory
Instructions
Data
Program Counter (PC) Register – Address of the next machine code instruction
Current Instruction Register (CIR)
The decoder looks at the bits of the CIR and using gates activates the correct ALU Element and register
The Clock causes the logic when to compute and when to copy results back to the register
PC
CIR
Decoder
https://en.wikipedia.org/wiki/Binary_decoder

## Slide 6: Machine Language Instructions
As part of the documentation for a CPU, we are given the bit patterns of the machine code for each of its instructions
There is usually a symbolic language that translates to machine language (assembler)
Assembly | Opcode | Description
CLX | 11100010 | Clear X register (X = 0).
INX | 11101000 | Increment X register by 1
LDX #value | 10100010 | Load X register with immediate (constant) value
LDX $address | 10100110 | Load X register from zero-page memory address
STX $address | 10000110 | Store X register to zero-page memory address

## Slide 7: Let's learn Base-16 (Hexadecimal)
Base 16 is easy to convert to bits and much less verbose than Base-2

## Slide 8: Recall Base-2
Base–2 to Base-10 for numbers less than 8
A.k.a. 3-bit numbers
Base-10 | Base-2
0 | 0
1 | 1
2 | 10
3 | 11
4 | 100
5 | 101
6 | 110
7 | 111
1 1 0 = 6
4s 2s 1s

## Slide 9: The first problem with Base-16
We only have 0-9 and we need to be able to represent 0-15 in a single base-16 digit
Thankfully we have emoji's
  10 ✊
  11 ☝️
  12 ✌️
  13 🤟 (also Rock on!)
  14 🍀
  15 🖐
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | ✊
11 | 1011 | ☝️
12 | 1100 | ✌️
13 | 1101 | 🤟
14 | 1110 | 🍀
15 | 1111 | 🖐

## Slide 10: AI suggested these emoji's
AI suggested emoji's
  10 🔟
  11 ⏸️
  12 🕛
  13 🕐 (1PM is 1300 hours)
  14 🕑 (2PM is 1400 hours)
  15 🕒 (3 PM is 1500 hours)
American Sign Language(ASL) uses one hand but requires motion
British Sign Language is different
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | 🔟
11 | 1011 | ⏸️
12 | 1100 | 🕛
13 | 1101 | 🕛
14 | 1110 | 🕑
15 | 1111 | 🕒

## Slide 11: No emojis in 1940 😭📅😭
We only have 0-9 as numbers and we need to be able to represent 0-15 in a single base-16 digit
So we used A-F to represent 10-15 for base-16 numbers
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 12: Base-10 and Base-16 (Hexadecimal) numbers
Need a cheat sheet
Base-10
12310 = 1 x 102 + 2 x 101 + 3 * 100
= 1 x 100 + 2 * 10 + 3 * 1 = 12310
Base-16
7B16 = 7 * 161 + 11 * 160 =
= 112 + 11 = 12310
Base-10 | Base-16
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F

## Slide 13: Base-16 to/from Base-2
Since 2 and 16 are even powers of 2, each Base-16 represents exactly four base-2 digits so we can convert digit by digit
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F
7B 16
0111 1011 2
A2 16
1010 0010 2
Hex is just more succinct Base-2

## Slide 14: Keep it simple for now
Go through base-10 if it helps
1 0 1 0 = 1010 = A16
1 0 0 0 = 810 = 816
1 1 1 1 = 1510 = F16
8s 4s 2s 1s
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 15: Chuck's not-so-quick Guide to Base-16
F16 = 1510 = 11112 (Easy one less than 16)
E16 = 1410 = 11102 (one less than 15)
A16 = 1010 = 10102 (8+2)
B16 = 1110 = 10112 (8+2+1)
C16 = 😕 🧠 🤟 = 8+4 = 11002
D16 = 😕 🤔 ⬆️ ⬇️ 🧠 📝 😠
AI: What is a good way to be able to do hex to base 2 conversions in your head?

## Slide 16: ASCII – 8 Bits
https://en.wikipedia.org/wiki/ASCII
http://www.catonmat.net/download/ascii-cheat-sheet.png
https://www.ca4e.com/tools/ascii/
ASCII Characters are 8-bits and can be nicely represented with two hex digits (a.k.a. nibbles)
American Standard Code for Information Interchange

## Slide 17
http://unicode.org/charts/

## Slide 18: Multi-Byte Characters (a quick aside…)
To represent the wide range of characters computers must handle we represent characters with more than one byte
  UTF-32 – Fixed Length - Four Bytes
  UTF-16 – Fixed length - Two bytes
  UTF-8 – 1-4 bytes
    - Upwards compatible with ASCII
    - Automatic detection between ASCII and UTF-8
    - UTF-8 is recommended practice for encoding data to be exchanged between systems
https://en.wikipedia.org/wiki/UTF-8

## Slide 19: What is Programming?
Hint: In the end any program we can write can also be represented in machine language. Machine code will both be simpler and a lot more complex. There is a reason we built languages like C and Python.

## Slide 20
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
11100010
11101000
Python for Everybody
Chapter 1
Slide 19
www.py4e.com
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 22: Program Steps or Program Flow
Like a recipe or installation instructions, a program is a sequence of steps to be done in order.
Some steps are conditional - they may be skipped.
Sometimes a step or group of steps is to be repeated.
Sometimes we store a set of steps to be used over and over as needed several places throughout the program

## Slide 23: Sequential Steps
Program:
x = 2
print(x)
x = x + 2
print(x)
Output:
2
4
x = 2
print(x)
x = x + 2
print(x)
When a program is running, it flows from one step to the next. As programmers, we set up “paths” for the program to follow.

## Slide 24: Conditional Steps
Output:
Smaller
Finis
Program:
x = 5
if x < 10:
print('Smaller')
if x > 20:
print('Bigger')
print('Finis')
x = 5
x < 10 ?
print('Smaller')
x > 20 ?
print('Bigger')
print('Finis')
Yes
No
No
Yes

## Slide 25: Repeated Steps
Output:
5
4
3
2
1
Blastoff!
Program:
n = 5
while n > 0 :
print(n)
n = n – 1
print('Blastoff!')
n > 0 ?
Loops (repeated steps) have iteration variables that change each time through a loop.
No
print('Blastoff')
Yes
n = 5
print(n)
n = n -1

## Slide 26: Variables
A variable is a named place in the memory where a programmer can store data and later retrieve the data using the variable “name”
Programmers get to choose the names of the variables
You can change the contents of a variable in a later statement
12.2
x
14
y
100
x = 12.2
y = 14
x = 100

## Slide 27: The CDC6504 Architecture
A blend of two names to avoid confusion with the actual MOS6502. And they both have registers named "X"

## Slide 28: MOS Technology 6502
Launched in 1975 and cost $25
4,528 NMOS Transistors
1Mhz
https://en.wikipedia.org/wiki/MOS_Technology_6502
Apple I, Apple II, Commodore PET, Commodore VIC-20, Commodore 64 (6510), Atari 2600, Atari 400, Atari 800, Atari XL series, Atari XE series, BBC Micro, Acorn Atom, Acorn Electron, Nintendo NES (2A03), Oric-1, Oric Atmos, Philips P2000, Ohio Scientific Challenger 1P, KIM-1 …

## Slide 29: Homage to the the CDC 6500
Control Data Corporation
Also in the mid-1970's
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 30: Homage to the the CDC 6500
Control Data Corporation
Also in the mid-1970’s
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
  Pascal
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 31: CDC6504 Architecture
0
Z
0x00
PC
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Data Memory
PC – Program Counter
ACC - Accumulator
Z – Was the last ACC result zero?
N – Was the last ACC result negative?
X and Y – Index registers
Instruction memory shown in base-2 for easy decoding
Data memory shown in hex – will usually contain ASCII
0
N
0x00
ACC
0x00
X
0x00
Y
What
Next?

## Slide 32: Programming the CDC6504
Assembly language is easier to read and translates directly to binary machine language
Assembly language also has labels, so we don't need to hand-compute the hex value of data or instruction address locations
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Opcode | Description
CLX | 11100010 | Clear X register (X = 0).
INX | 11101000 | Increment X register by 1
LDX #value | 10100010 | Load X register with immediate (constant) value
LDX $address | 10100110 | Load X register from zero-page memory address
STX $address | 10000110 | Store X register to zero-page memory address

## Slide 33: Our first Program
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
0x00
0x06
00000000
0x06
CLX ; Clear X register
INX ; Increment X
INX ; Increment X again
BRK
0
Z
0x00
PC
0
N
0x00
ACC
0x00
X
0x00
Y

## Slide 34: Our first Program
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
0x00
0x06
00000000
0x06
CLX ; Clear X register
INX ; Increment X
INX ; Increment X again
BRK
0
Z
0x00
PC
0
N
0x00
ACC
0x00
X
0x00
Y

## Slide 35: Our first Program
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
0x00
0x06
00000000
0x06
CLX ; Clear X register
INX ; Increment X
INX ; Increment X again
BRK
0
Z
0x01
PC
0
N
0x00
ACC
0x01
X
0x00
Y

## Slide 36: Our first Program
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
0x00
0x06
00000000
0x06
CLX ; Clear X register
INX ; Increment X
INX ; Increment X again
BRK
0
Z
0x02
PC
0
N
0x00
ACC
0x02
X
0x00
Y

## Slide 37: Our first Program
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
0x00
0x06
00000000
0x06
CLX ; Clear X register
INX ; Increment X
INX ; Increment X again
BRK
0
Z
0x03
PC
0
N
0x00
ACC
0x02
X
0x00
Y

## Slide 38: Our CPU from Logic, Gates, Transistors
There is a lot of overlap between the CDC6504 and our two instruction CPU….

## Slide 39: Our CPU from Logic, Gates, Transistors
Our CPU implements two instructions
  Zero Register
  Increment Register
There is no program counter because there is no instruction memory
But….
Increment
Register
Instruction
Decode
Logic

## Slide 40: Looking closer
These two instructions are the equivalent to the zero (clear the latch) and one (increment the latch) from our hand-built CPU
The 6502 has 8-bit registers
11100010
11101000
CLX ; Clear X register
INX ; Increment X

## Slide 41: If you had time…
With what you know and and better design tools you could design a CDC6504
  Logic
  Memory
  VLSI layout
  Manufacture

## Slide 42: CDC6504 Machine Language
https://www.ca4e.com/cdc6504/documentation.html

## Slide 43: CDC6504 Architecture
0
Z
0x00
PC
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Data Memory
PC – Program Counter
ACC - Accumulator
Z – Was the last ACC result zero?
N – Was the last ACC result negative?
X and Y – Index registers
Instruction memory shown in base-2 for easy decoding
Data memory shown in hex – will usually contain ASCII
0
N
0x00
ACC
0x00
X
0x00
Y
What
Next?

## Slide 44: Index Instructions (8-bit)
The X and Y registers are often used to control counted loops or to be an offset within an array.
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Opcode | Description
CLX | 11100010 | Clear X register (X = 0). Sets Z flag to 1, N flag to 0.
CLY | 11000010 | Clear Y register (Y = 0). Sets Z flag to 1, N flag to 0s.
INX | 11101000 | Increment X register by 1
INY | 11001000 | Increment Y register by 1
DEX | 11001010 | Decrement X register by 1
DEY | 10001000 | Decrement Y register by 1

## Slide 45: 16-Bit Instructions
The byte immediately following the instruction can be a constant value or data memory address
https://www.ca4e.com/tools/cdc6504/documentation.html
10000101
0x00
00101010
0x01
LDA #'*'
(the 42)
Assembly | Opcode | Description
LDA #value | 10101001 | Load accumulator with immediate value (0-255, 0x00-0xFF, or 'A')
LDA $address | 10100101 | Load accumulator using immediate value as memory address
10100101
0x02
00000010
0x03
LDA $02
(the address 2)

## Slide 46: Load / Store Instructions
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Opcode | Description
LDA #value | 10101001 | Load accumulator with immediate value (ACC = value)
LDA $address | 10100101 | Load accumulator from zero-page memory address (ACC = memory[address])
LDX #value | 10100010 | Load X register with immediate value (X = value)
LDX $address | 10100110 | Load X register from zero-page memory address (X = memory[address])
LDY #value | 10100000 | Load Y register with immediate value (Y = value)
STA $address | 10000101 | Store accumulator to zero-page memory address (memory[address] = ACC)
STX $address | 10000110 | Store X register to zero-page memory address (memory[address] = X)
STY $address | 10000100 | Store Y register to zero-page memory address (memory[address] = Y)

## Slide 47: Arithmetic Instructions
Adding and subtraction and getting back a result is ACC only
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Opcode | Description
ADC #value | 01101001 | Add (immediate): ACC = ACC + value
ADC $address | 01100101 | Add (from memory): ACC = ACC + memory[address]
SBC #value | 11101001 | Subtract (immediate): ACC = ACC - value
SBC $address | 11100101 | Subtract (from memory): ACC = ACC - memory[address]

## Slide 48: Comparison Instructions
Comparison is like doing a subtraction, setting Z and N and then discarding the result of the subtraction.
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Opcode | Description
CMP #value | 11001001 | Compare accumulator with immediate value, sets Z, N flags
CMP $address | 11000101 | Compare accumulator with memory[address], sets Z, N flags
CPX #value | 11100000 | Compare X register with immediate value, sets Z, N flags
CPX $address | 11100100 | Compare X register with memory[address], sets Z, N flags
CPY #value | 11000000 | Compare Y register with immediate value, sets Z, N flags
CPY $address | 11000100 | Compare Y register with memory[address], sets Z, N flags

## Slide 49: There is no IF statement in Machine Code
Every instruction that changes a register (and the compare instructions) sets the result flags
  Z = 1 if the result is zero, 0 if the result is no zero
  N = 1 if the result is negative and 0 if the result is positive
The CMP instruction is like subtraction – it sets Z and N but ignores the result value of the subtraction
https://www.ca4e.com/tools/cdc6504/documentation.html
Result | Z | N
0 | 1 | 0
positive | 0 | 1
negative | 0 | 0

## Slide 50: There is no IF statement in Machine Code
The closest we have to an IF is a CMP + conditional jump
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Opcode | Description
BEQ $address | 11110000 | Branch if equal (Z flag set)
BNE $address | 11010000 | Branch if not equal (Z flag clear)
BMI $address | 00110000 | Branch if minus (N flag set)
BPL $address | 00010000 | Branch if plus (N flag clear)
LDA #'p' ; ASCII value for 'p'
CMP #'a' ; ASCII value for 'a'
BMI $08 ; Branch if minus (less than)
SBC #0x20 ; convert to uppercase
BRK ; This is at 0x08
if acc < 'a' : goto skip
acc = acc – 0x20
skip: BRK

## Slide 51
10000110
0x00
01110000
0x01
LDA #'p'
(the 'p')
10001110
0x02
01100001
0x03
CMP #'a'
(the 'a')
10100001
0x04
00001000
0x05
BMI $08
(the 0x08)
10000101
0x06
00101010
0x07
SBC #0x20
(the 0x20)
00000000
0x08
BRK
ACC = 'p'
Yes
ACC ? 'a'
N?
ACC = ACC–0x20
Halt
No
Notes: This is a simple program to check if a character ('p') is already upper case. If it is not upper case, we subtract 0x20 from the ASCII value to convert it to upper case. At the end of the program, X2 contains the upper-case value whether the initial value was an upper- or lower-case letter. The result in X2 is 'P' (upper-case)

## Slide 52: Assembly gives us labels
No need to compute instruction addresses by hand
LDA #'p'
CMP #'a'
BMI skip
SBC #0x20
skip:
BRK
10000110
0x00
01110000
0x01
LDA #'p'
(the 'p')
10001110
0x02
01100001
0x03
CMP #'a'
(the 'a')
10100001
0x04
00001000
0x05
BMI 0x08
(the 0x08)
10000101
0x06
00101010
0x07
SBC #0x20
(the 0x20)
00000000
0x08
BRK

## Slide 53: Jumps are far simpler than "if logic"
You can think of the unconditional Jump as a SET of the Program Counter (PC) register
A conditional jump is a conditional set of the PC register
Assembly | Opcode | Description
JMP $address | 01001100 | Unconditional jump to absolute address (zero-page)
BEQ $address | 11110000 | Branch if equal (Z flag set)
BNE $address | 11010000 | Branch if not equal (Z flag clear)
BMI $address | 00110000 | Branch if minus (N flag set)
BPL $address | 00010000 | Branch if plus (N flag clear)

## Slide 54: There is no "for" or "while" in machine language
CLX ; Clear X register
loop:
CPX #5 ; Compare X to 5
BEQ end ; Branch if equal (Z flag set)
INX ; Increment X
JMP loop ; Jump to loop
end:
BRK ; Halt
X = 0
Yes
X ? 5
Z ?
JMP loop
BRK
No
X = X + 1

## Slide 55
https://www.ca4e.com/tools/cdc6504/documentation.html
Assembly | Opcode | Description
CLX | 11100010 | Clear X register (X = 0). Sets Z flag to 1, N flag to 0.
INX | 11101000 | Increment X register by 1
LDA #value | 10101001 | Load accumulator with immediate value (ACC = value)
LDA $address | 10100101 | Load accumulator (ACC = memory[address])
STA $address | 10000101 | Store accumulator (memory[address] = ACC)
ADC #value | 01101001 | Add (immediate): ACC = ACC + value
SBC $address | 11100101 | Subtract (from memory): ACC = ACC - memory[address]
CMP #value | 11001001 | Compare accumulator with immediate value, sets Z, N flags
JMP $address | 01001100 | Unconditional jump to absolute address (zero-page)
BEQ $address | 11110000 | Branch if equal (Z flag set)
BMI $address | 00110000 | Branch if minus (N flag set)
BRK | 00000000 | Break/Halt - Stop program execution

## Slide 56: CDC 6504 – Assembly Language
https://www.ca4e.com/cdc6504/documentation.html

## Slide 57: CDC6504 Architecture
0
Z
0x00
PC
11100010
0x00
11101000
0x01
11101000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Data Memory
PC – Program Counter
ACC - Accumulator
Z – Was the last ACC result zero?
N – Was the last ACC result negative?
X and Y – Index registers
Instruction memory shown in base-2 for easy decoding
Data memory shown in hex – will usually contain ASCII
0
N
0x00
ACC
0x00
X
0x00
Y
What
Next?

## Slide 58: Data Directive – Assembly Only
Assembly | Description
DATA 'string' | Pre-populates data memory (not instruction memory) with a null-terminated string. Data is loaded starting at memory address 0.
DATA 0x00 0x0A ... | Pre-populates data memory (not instruction memory) with a space-separated list of hexadecimal values. Data is loaded starting at memory address 0.

## Slide 59: Add 5 + 15 and Store
LDA #10 ; Load 10 into accumulator
ADC #5 ; Add 5 (result = 15)
STA $00 ; Store result to memory[0]
BRK

## Slide 60: Conditional convert to upper case
LDA #'p' ; 0x70 is the ASCII value for 'p'
CMP #'a' ; 0x61 is the ASCII value for 'a'
BMI skip ; Branch if minus (less than)
SBC #0x20 ; Subtract 0x20 to convert to uppercase
skip:
BRK

## Slide 61: Print Hello
LDA #'H' ; Load 'H' into accumulator
STA $00
LDA #'e' ; Load 'e' into accumulator
STA $01
LDA #'l' ; Load 'l' into accumulator
STA $02
STA $03 ; Store 'l' again
LDA #'o' ; Load 'o' into accumulator
STA $04
BRK

## Slide 62: Count to Five
CLX ; Clear X register
loop:
CPX #5 ; Compare X register to 5 (simpler than TXA/CMP)
BEQ end ; Branch if equal (Z flag set)
INX ; Increment X
JMP loop ; Jump to loop
end:
BRK ; Halt

## Slide 63: CPU Emulators are Thing
Not just for learning any more…

## Slide 64
// Load instructions (immediate mode)
else if (instruction === 0xA9) { // LDA # - Load accumulator immediate
const immediate = this.cpu.instructions[this.cpu.pc + 1];
this.cpu.acc = immediate;
this.updateCompareFlags(this.cpu.x, immediate);
pcIncrement = 2;
} else if (instruction === 0xA2) { // LDX # - Load X immediate
const immediate = this.cpu.instructions[this.cpu.pc + 1];
this.cpu.x = immediate;
this.updateCompareFlags(this.cpu.x, immediate);
pcIncrement = 2;
} else if (instruction === 0xE9) { // SBC # - Subtract immediate
const immediate = this.cpu.instructions[this.cpu.pc + 1];
const diff = this.cpu.acc - immediate;
this.cpu.acc = diff & 0xFF;
this.updateStatusFlags(this.cpu.acc);
pcIncrement = 2;
}
https://www.ca4e.com/tools/cdc6504/cpu-emulator.js

## Slide 65: Building Emulators for Historical CPUs
It is not all that difficult to build an emulator for an older (simpler) CPU
Modern processors on our phones and computers are so fast that JavaScript in a browser can emulate historical machine code faster than the original hardware
The computer / phone / browser graphics are also far better
And it can be great fun

## Slide 66: Archive.org: Internet Arcade

## Slide 67: Game: Dig Dug

## Slide 68: Dig Dug Startup – JSMAME Emulator

## Slide 69: WASM – Web Assembly
There is a machine language emulator built into browsers called Web Assembly
For a wide range of software, compiling to WASM and running in JavaScript is enough
WASM is a different syntax than most Assembly languages – but it still compiles to a binary-machine code
C Programming for Everybody (www.cc4e.com) C Playground compiles C to WASM and then runs the WASM in the user's browser

## Slide 70: WASM Hello World
;; Hello World WASM Example
(module
(import "console" "log" (func $log (param i32 i32)))
(memory 1)
(data (i32.const 0) "Hello, World!")
(func $main (result i32)
(call $log (i32.const 0) (i32.const 13))
(i32.const 42)
)
(export "main" (func $main))
)
00000000: 00 61 73 6d 01 00 00 00 01 0a 02 60 02 7f 7f 00 |.asm.......`....|
00000010: 60 00 01 7f 02 0f 01 07 63 6f 6e 73 6f 6c 65 03 |`.......console.|
00000020: 6c 6f 67 00 00 03 02 01 01 05 03 01 00 01 07 11 |log.............|
00000030: 02 06 6d 65 6d 6f 72 79 02 00 04 6d 61 69 6e 00 |..memory...main.|
00000040: 01 0a 0c 01 0a 00 41 00 41 0d 10 00 41 2a 0b 0b |......A.A...A*..|
00000050: 13 01 00 41 00 0b 0d 48 65 6c 6c 6f 2c 20 57 6f |...A...Hello, Wo|
00000060: 72 6c 64 21 |rld!|

## Slide 72: CPU Evolution
At this point, with a bit more study, and manufacturing facilities you might know enough to build the Apple I

## Slide 74: Apple Computer Processors over time
MOS 6502 – Apple I / Apple II – 1977 - 1993
Motorola MC68000 – Macintosh 1984-1994
ARM – Apple Newton - 1993
IBM PowerPC – Macintosh 1994 – 2006
Intel x86 – Macintosh (2006-2020)
Samsung ARM – iPhone (2007-2009)
Apple ARM – iPhone (2010-Present)
Apple ARM – Macintosh (2020-Present)
Apple currently redesigns their CPUs based on workload over time – Image Processing / Audio / Video / Gaming / Artificial Intelligence

## Slide 75: Fun Aside – the 6502 influenced ARM
Acorn's 6502-based BBC Micros
The ARM designers were 6502 experts
The BBC Micro was used to build and simulate the ARM design
ARM1 had ~25,000 transistors
AI: Describe the historical connection between the 6502, ARM, and Raspberry Pi
https://en.wikipedia.org/wiki/Sophie_Wilson

## Slide 76: Summary
Fetch-Decode-Execute (a.k.a. Fetch-Execute-Cycle)
Look at the Intel x86 and ARM processor families
Explored the CDC6504 architecture, instruction set, assembly and machine languages
Explored an increasing use of in-browser emulators for games and other applications
Web Assembly (WASM)
CPU Evolution over time

## Slide 77: Acknowledgements / Contributions
These slides are Copyright 2025- Charles R. Severance (online.dr-chuck.com) as part of www.ca4e.com and made available under a Creative Commons Attribution 4.0 License. Please maintain this last slide in all copies of the document to comply with the attribution requirements of the license. If you make a change, feel free to add your name and organization to the list of contributors on this page as you republish the materials.
Initial Development: Charles Severance, University of Michigan School of Information
Insert new Contributors and Translators here including names and dates
Continue new Contributors and Translators here