## Slide 1: The CDC 8512 Microprocessor
Dr. Charles R. Severance
online.dr-chuck.com

## Slide 2: Outline
Our two-instruction "CPU" - What is missing?
Instruction decoding and control
Real CPUs
The CDC8512 – inspired by the CDC 6500
Emulators – JavaScript – Old video Games at archive.org
Reading: Evolution of CPU Architecture
Reading: Intel 4004 – Back to the beginning

## Slide 3: What is missing?
The instructions are not being read from memory.
It is like there is a switch on the front of the computer and it chooses between the two instructions
We want a flexible sequence of many combinations of instruction sequences(a.k.a. Software)

## Slide 4
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Python for Everybody
Chapter 1
Slide 19
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 5: Fetch-Decode-Execute-Cycle
CPU
ALU
Registers
Cache / Memory
Instructions
Data
Program Counter (PC) Register – Address of the next machine code instruction
Current Instruction Register (CIR)
The decoder looks at the bits of the CIR and using gates activates the correct ALU Element and register
The Clock causes the logic when to compute and when to copy results back to the register
PC
CIR
Decoder
https://en.wikipedia.org/wiki/Binary_decoder

## Slide 6: Machine Language Instructions
As part of the documentation for a CPU, we are given the bit patterns of the machine code for each of its instructions
There is usually a symbolic language that translates to machine language (assembler)
Assembly Language | Binary | Description
ZERO reg | 01000rrr | Set register to zero
CMPZ reg | 01001rrr | Compare register to zero
INC reg | 01010rrr | Increment register by 1
DEC reg | 01011rrr | Decrement register by 1

## Slide 7: Let's learn Base-16 (Hexadecimal)
Base 16 is easy to convert to bits and much less verbose than Base-2

## Slide 8: Recall Base-2
Base–2 to Base-10 for numbers less than 8
A.k.a. 3-bit numbers
Base-10 | Base-2
0 | 0
1 | 1
2 | 10
3 | 11
4 | 100
5 | 101
6 | 110
7 | 111
1 1 0 = 6
4s 2s 1s

## Slide 9: The first problem with Base-16
We only have 0-9 and we need to be able to represent 0-15 in a single base-16 digit
Thankfully we have emoji's
  10 ✊
  11 ☝️
  12 ✌️
  13 🤟 (also Rock on!)
  14 🍀
  15 🖐
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | ✊
11 | 1011 | ☝️
12 | 1100 | ✌️
13 | 1101 | 🤟
14 | 1110 | 🍀
15 | 1111 | 🖐

## Slide 10: No emojis in 1940 😭📅😭
We only have 0-9 as numbers and we need to be able to represent 0-15 in a single base-16 digit
So we used A-F to represent 10-15 for base-16 numbers
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 11: Base-10 and Base-16 (Hexadecimal) numbers
Need a cheat sheet
Base-10
12310 = 1 x 102 + 2 x 101 + 3 * 100
= 1 x 100 + 2 * 10 + 3 * 1 = 12310
Base-16
7B16 = 7 * 161 + 11 * 160 =
= 112 + 11 = 12310
Base-10 | Base-16
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F

## Slide 12: Base-16 to/from Base-2
Since 2 and 16 are even powers of 2, each Base-16 represents exactly four base-2 digits so we can convert digit by digit
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F
7B 16
0111 1011 2
A2 16
1010 0010 2
Hex is just more succinct Base-2

## Slide 13: Keep it simple for now
Go through base-2 if it helps
1 0 1 0 = 10 = A
1 0 0 0 = 8 = 8
1 1 1 1 = 15 = F
8s 4s 2s 1s
Base-10 | Base-2 | Base-16
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 14: Chuck's Not-so-quick Guide to Base-16
F16 = 1510 = 11112 (Easy one less than 16)
E16 = 1410 = 11102 (one less than 15)
A16 = 1010 = 10102 (8+2)
B16 = 1110 = 10102 (8+2+1)
C16 = 😕 🧠 🤟 = 8+3 = 10112
D16 = 😕 🤔 ⬆️ ⬇️ 🧠 📝 😠
AI: What is a good way to be able to do hex to base 2 conversions in your head?

## Slide 15: ASCII – 8 Bits
https://en.wikipedia.org/wiki/ASCII
http://www.catonmat.net/download/ascii-cheat-sheet.png
ASCII Characters are 8-bits and can be nicely represented with two hex digits (a.k.a. nibbles)
American Standard Code for Information Interchange

## Slide 16: Multi-Byte Characters (a quick aside…)
To represent the wide range of characters computers must handle we represent characters with more than one byte
  UTF-16 – Fixed length - Two bytes
  UTF-32 – Fixed Length - Four Bytes
  UTF-8 – 1-4 bytes
    - Upwards compatible with ASCII
    - Automatic detection between ASCII and UTF-8
    - UTF-8 is recommended practice for encoding data to be exchanged between systems
https://en.wikipedia.org/wiki/UTF-8

## Slide 17: A Very Simple CPU
The CDC8512 is designed to be understandable

## Slide 18: Why wouldn't we use a real CPU?
Intel X86 – Introduced in 1978
  Focused on Desktop computers
  Includes AMD
ARM – Introduced in 1985
  Focused on early cell phones
  Core Instruction Set + Extensions
Real CPUs are quite intricate because over time they added new instructions and kept the old ones for compatibility.

## Slide 19: ARM Assembly
.global _start
_start:
MOV R0, #3 @ Load 3 into R0
MOV R1, #4 @ Load 4 into R1
ADD R0, R0, R1 @ R0 = R0 + R1 (3 + 4 = 7)
MOV R7, #1 @ syscall: exit
SWI 0 @ exit with code in R0 (7)

## Slide 20: Intel X86 Assembly
global _start
_start:
mov eax, 3 ; Load 3 into eax
mov ebx, 4 ; Load 4 into ebx
add eax, ebx ; eax = eax + ebx (3 + 4 = 7)
mov ebx, eax ; exit code = sum (7)
mov eax, 1 ; syscall number for exit
int 0x80 ; make syscall

## Slide 21: CDC 8512 - Inspired by CDC 6500
Control Data Corporation
Mid 1960’s – mid-1970’s
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 22: CDC 8512 - Inspired by CDC 6500
Control Data Corporation
Mid 1960’s – mid-1970’s
Dr. Chuck’s first computer
  FORTRAN
  Assembly Language
  Pascal
https://en.wikipedia.org/wiki/CDC_6000_series#Central_processor

## Slide 23: About the CDC6500
60 bit words – Integer and floating point formats
6 bit characters - upper case only
Two kinds of data registers - A0-A7 – Address and X0-X7 Operands
To load from memory you put the address in A1-A5 and the data from memory is loaded into the corresponding X1-X5
To store into memory you put the data in X6 or X7 and Set the corresponding A6 or A7 to the location where you want the memory stored

## Slide 24
http://ygdes.com/CDC/60100000D_6600refMan_Feb67.pdf
To provide a more compact symbolic language, the 24 operating registers are identified by letters and numbers:
A = Address Register (A0, A1 .. A7)
B = increment register (B0, B1 … B7)
X = operand register (X0, X1 … X7)
The operand registers hold operands and results for servicing the functional units. Five registers (X1-X5) hold read operands from Central Memory and two registers X6 – X7) hold results to be sent to Central Memory (Figure 3-2).
Operands and results transfer between memory and these registers as a result of placing a quantity into a corresponding address register (A1-A7).
-- Control Data 6400/6500/6660 Computer Systems Reference Manual
Figure 3.2

## Slide 25: About the CDC8512
8 bit words – Positive integers only (i.e. like a C char)
8 bit characters – ASCII (i.e. like a C char)
32 bytes of Instruction memory and 32 bytes of Data memory
Eight 8-bit registers (A0-A3) and (X0-X3)
When A0 is set it causes a load from Data[A0] into X0 to happen
When A1 is set it causes a load from Data[A1] into X1 to happen
When A2 is set it causes a store from X2 into Data[A2] to happen
When A3 is set it causes a store from X3 into Data[A3] to happen

## Slide 26: CDC8512 Architecture
0x00
A0
0x00
PC
<=>
CMP
00000000
0x00
00000000
0x01
00000000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Data Memory
PC – Program Counter
CMP – Result of most recent comparison
Mode – Error indicator
A and X registers shown in hex
Instruction memory shows in base-2 for easy decoding
Data memory shows in hex – will usually contain ASCII
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3
What
Next?

## Slide 27: What is Programming? Python for Everybody www.py4e.com

## Slide 28
Software
Input
and Output
Devices
Central
Processing
Unit
Main
Memory
Secondary
Memory
Generic
Computer
What
Next?
Machine
Language
01001001
00111001
Python for Everybody
Chapter 1
Slide 19
Notes: This slide is a block diagram of a computer showing a central processing unit connected to main memory. Software is loaded into the main memory. The software can also interact with input / output devices and secondary memory for long-term storage.

## Slide 29: Variables
A variable is a named place in the memory where a programmer can store data and later retrieve the data using the variable “name”
Programmers get to choose the names of the variables
You can change the contents of a variable in a later statement
12.2
x
14
y
100
x = 12.2
y = 14
x = 100

## Slide 30: The True Story of Python Assignment Statements
Charles Severance
www.dj4e.com

## Slide 31: Program Steps or Program Flow
Like a recipe or installation instructions, a program is a sequence of steps to be done in order.
Some steps are conditional - they may be skipped.
Sometimes a step or group of steps is to be repeated.
Sometimes we store a set of steps to be used over and over as needed several places throughout the program

## Slide 32: Sequential Steps
Program:
x = 2
print(x)
x = x + 2
print(x)
Output:
2
4
x = 2
print(x)
x = x + 2
print(x)
When a program is running, it flows from one step to the next. As programmers, we set up “paths” for the program to follow.

## Slide 33: Conditional Steps
Output:
Smaller
Finis
Program:
x = 5
if x < 10:
print('Smaller')
if x > 20:
print('Bigger')
print('Finis')
x = 5
x < 10 ?
print('Smaller')
x > 20 ?
print('Bigger')
print('Finis')
Yes
No
No
Yes

## Slide 34: Repeated Steps
Output:
5
4
3
2
1
Blastoff!
Program:
n = 5
while n > 0 :
print(n)
n = n – 1
print('Blastoff!')
n > 0 ?
Loops (repeated steps) have iteration variables that change each time through a loop.
No
print('Blastoff')
Yes
n = 5
print(n)
n = n -1

## Slide 35: Variables and Sequential Programming

## Slide 36: Variables in Machine Language
There are no variables in machine language
There are no objects
There is no "dynamic memory allocation"
There are constants like 42, '*', and 123
We have a limited number of named registers in the CPU
There is one big array of memory locations
  Memory is like one big array in C
  Memory addresses are like pointers in C

## Slide 37: CDC8512 Variables
0x00
A0
0x00
PC
<=>
CMP
00000000
0x00
00000000
0x01
00000000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Data Memory
Address Registers (4) are for load / store addresses
X registers (4) are for data and computations and for load / store data
Data memory (255) holds variables when we want to reuse a register
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3

## Slide 38: Load / Store
0x00
A0
0x00
PC
<=>
CMP
00000000
0x00
00000000
0x01
00000000
0x02
00000000
0x03
00000000
0x04
00000000
0x05
Instruction Memory
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Data Memory
PC – Program Counter
CMP – Result of most recent comparison instruction
Mode – Error indicator
A and X registers shown in hex
Instruction memory is shown in base-2 for easy decoding
Data memory shows in hex – will usually contain ASCII
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3
What
Next?

## Slide 39: CDC8512 Architecture
0x00
A0
0x00
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
A program
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3
0x00
0x06
00000001
0x06
Set register X2 to the next byte
The letter 'H'
Set A2 to 0 (Stores X2 at 0x00)
Set register X2 to the next byte
The letter 'i'
Add 1 to A2 (Stores X2 at 0x01)
Halt and Print

## Slide 40: CDC8512 Architecture
0x00
A0
0x00
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Start the program
Out first instruction is a two byte instruction
  0x00 Sets X2 to the byte at 0x01
  Advances the PC by 2
The byte at 0x01 is the ASCII letter for 'H' (0x68)
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x00
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 41: CDC8512 Architecture
0x00
A0
0x02
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x00
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
Start the program
Out first instruction is a two byte instruction
  0x00 Sets X2 to the byte at 0x01
  Advances the PC by 2
The byte at 0x01 is the ASCII letter for 'H' (0x68)
So 'H' is loaded into X2 and the PC is set to 0x02
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x48
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 42: CDC8512 Architecture
0x00
A0
0x02
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x48
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
We load the instruction at 0x02
Which sets A0 to 0 and as a side effect, stores the contents of X2 into data location 0x00
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x48
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 43: CDC8512 Architecture
0x00
A0
0x03
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x48
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
We load the instruction at 0x02
Which sets A0 to 0 and as a side effect, stores the contents of X2 into data location 0x00
Then the PC is updated to 0x03
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x48
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 44: CDC8512 Architecture
0x00
A0
0x03
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x48
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
The instruction at 0x03 is a two byte instruction
  0x03 Sets X2 to the byte at 0x04
  Advances the PC by 2
The byte at 0x04 is the ASCII letter for 'i' (0x89)
So 'i' is loaded into X2
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x69
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 45: CDC8512 Architecture
0x00
A0
0x05
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x48
0x00
0x00
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
The instruction at 0x03 is a two byte instruction
  0x03 Sets X2 to the byte at 0x04
  Advances the PC by 2
The byte at 0x04 is the ASCII letter for 'i' (0x89)
So 'i' is loaded into X2
And the PC is set to 0x05
0
Mode
0x00
A1
0x00
A2
0x00
A3
0x00
X0
0x00
X1
0x69
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 46: CDC8512 Architecture
0x00
A0
0x05
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x48
0x00
0x69
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
We load the instruction at 0x05
Which adds 1 to A0 and as a side effect, stores the contents of X2 into data location 0x00
Then the PC is updated to 0x06
0
Mode
0x00
A1
0x01
A2
0x00
A3
0x00
X0
0x00
X1
0x69
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 47: CDC8512 Architecture
0x00
A0
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x48
0x00
0x69
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
We load the instruction at 0x06
Which is a "Halt and Print" instruction
The memory contains a zero terminated string
  0x68 0x89 0x00
From the ASCII table, our output is "Hi"
0
Mode
0x00
A1
0x01
A2
0x00
A3
0x00
X0
0x00
X1
0x69
X2
0x00
X3
0x00
0x06
00000001
0x06

## Slide 48: Review
0x00
A0
0x06
PC
<=>
CMP
10000110
0x00
01001000
0x01
01000010
0x02
10000110
0x03
01101001
0x04
01010010
0x05
0x48
0x00
0x69
0x01
0x00
0x02
0x00
0x03
0x00
0x04
0x00
0x05
0
Mode
0x00
A1
0x01
A2
0x00
A3
0x00
X0
0x00
X1
0x69
X2
0x00
X3
0x00
0x06
00000001
0x06
Set register X2 to the next byte
The letter 'H'
Set A2 to 0 (Stores X2 at 0x00)
Set register X2 to the next byte
The letter 'i'
Add 1 to A2 (Stores X2 at 0x01)
Halt and Print
Hi

## Slide 49
Hi

## Slide 50: Comparison Register

## Slide 51: Low level language
What is a jump instruction - there is no if-then-else
There is no for or while loops - there is only compare and conditionally jump

## Slide 52: CDC 8512 – Instruction Set
https://www.ca4e.com/cdc8512/documentation.html

## Slide 53: CDC8512 CPU Reference

## Slide 54: Set a Register
SET X3, 'C' ; Set X3 to the value for ASCII C (67)
SET A3, 0 ; Set A3 to zero and store 'C' in data memory location 0x00
SET A1, 0 ; Set A1 to zero and load memory location 0x00 into X0
MOV X1, X3 ; Copy X3 to X1
SET A3, 0x01 ; Set A3 to 1 and store 'C' in data memory location 0x01
SET X3, 0x00 ; Set X3 to zero
SET A3, 0x02 ; Set A3 to 0x02 and store X3 into location 0x02
; Note constants can be decimal (0-255) hexadecimal (0x00-0xff) or a single
; ASCII character in single quotes 'a'

## Slide 55: Register Arithmetic
; This will print: Hello
SET X3, 'H' ; Set X3 to the value for ASCII H
SET A3, 0 ; Set A3 to zero and store 'H' in data memory location 0x00
SET X3, 'e' ; Set X3 to 'e'
INC A3 ; Add 1 to A3 and store 'e' in location 0x01
SET X3, 'l' ; Set X3 to 'l'
ADD A3, 1 ; Add 1 to A3 and store 'l' in location 0x02
INC A3 ; Add 1 to A3 and store 'l' in location 0x03
ADD X3, 4 ; Add 4 to X3 so that it is now 'p'
DEC X3 ; Subtract 1 from X3 so that it is now 'o'
INC A3 ; Add 1 to A3 and store '0' in location 0x04
SET X3, 0 ; Set X3 to integer zero
INC A3 ; Add 1 to A3 and store integer 0 in location 0x05
PS ; Print memory starting at data address 0 as an
; ASCII string, stopping when a zero is encountered

## Slide 56: Comparison and Jumps
JP 0x12 ; Set the PC (Program Counter) to an instruction address and
; continue execution at that address
CMP X3, 42 ; Compare a register to a constant and set comparison status
JE 0x12 ; Jump to the instruction address if comparison status is =
JG 0x12 ; Jump to the instruction address if comparison status is >
JL 0x12 ; Jump to the instruction address if comparison status is <

## Slide 57: Miscellaneous Instructions
PS # Print data area starting at specified data address
# stopping when an integer 0 byte is encountered
HALT # Stop Execution

## Slide 58: Summary
SX3 A3 # Copy a register to another
SX3 42 # Set a register to an 8-bit
INC A1 # Add 1 to a register
DEC X3 # Subtract 1 from a register
ADD X1, 42 # Add a constant to a register
SUB X3, 42 # Subtract a constant from a register
JP 0x12 # Jump to a label
CMP X3, 42 # Compare a register to a constant and set comparison status
JE 0x12 # Jump to the address if CMP was equal
JG 0x12 # Jump to the address if CMP was >
JL 0x12 # Jump to the address if CMP was <
PS # Print data area as character string
DI # Dump Instruction area in hex 16 per line
DD # Dump data area in hex 16 per
HALT # Stop Execution

## Slide 59: CDC 8512 – Machine Language
(a.k.a. the zeros and ones of programming)

## Slide 60: CDC 8512 - Assembly / Machine Code
SET X2, 'H'
ZERO A2
SET X2, 'i'
INC A2
PS
HALT
10000110
01001000 'H'
01000010
10000110
01101001 'i'
01010010
00000001
00000000

## Slide 61: Single Register 8-bit Instruction
0
1
0
0
0
0
1
0
ZERO A2
Register
Number
0 = A register
1 = X register
Register
Zero Register
Op Code

## Slide 62: Set Register to Constant (16-bit instruction)
1
0
0
0
0
1
1
0
SET X2,'H'
Register
Number
0 = A register
1 = X register
0
1
0
0
1
0
0
0
ASCII for 'H'
Set Register
Op Code

## Slide 63: Single Register 8-Bit Instruction
0
1
0
1
0
0
1
0
INC A2 # Increment A2
Register
Number
0 = A register
1 = X register
Register
Decrement Register
Op Code

## Slide 64: Print and Halt Instructions
0
0
0
0
0
0
0
0
PS # Print Memory
HALT # Stop the CPU
0
0
0
0
0
0
0
1

## Slide 65: Two Register Instruction
1
1
0
0
1
1
1
1
MV A1,X3 ; Copy A1 to X3
Register
Number
0 = A register
1 = X register
Register
Number
0 = A register
1 = X register
Destination
Register
Source
Register
Register
Copy

## Slide 66: CDC8512 Emulator in JavaScript
// 5-bit patterns (bits 7-3)
else if ((instruction >> 3) === 0x08) { // 01000xxx - ZERO
const register = instruction & 0x07;
const regName = this.getRegisterName(register);
this.cpu[regName] = 0;
// CDC 6500 load/store architecture:
if (regName === 'a0') {
this.cpu.x0 = this.cpu.memory[this.cpu.a0];
} else if (regName === 'a1') {
this.cpu.x1 = this.cpu.memory[this.cpu.a1];
} else if (regName === 'a2') {
this.cpu.memory[this.cpu.a2] = this.cpu.x2;
} else if (regName === 'a3') {
this.cpu.memory[this.cpu.a3] = this.cpu.x3;
}
pcIncrement = 1;
}

## Slide 67: Emulators for Fun

## Slide 68: Building Emulators for Historical CPUs
It is not all that difficult to build an emulator for an older (simpler) CPU
Modern processors on our phones and computers are so fast that JavaScript in a browser can emulate historical machine code faster than the original hardware
The computer / phone / browser graphics are also far better
And it can be great fun

## Slide 69: Archive.org: Internet Arcade

## Slide 70: Game: Dig Dug

## Slide 71: Dig Dug Startup – JSMAME Emulator

## Slide 72: CPU Evolution
Why we invented our own super simple processor to learn.

## Slide 73: Apple Computer Processors over time
MOS 6502 - Apple II – 1977 - 1993
Motorola MC68000 – Macintosh 1984-1994
IBM PowerPC – Macintosh 1994 – 2006
Intel x86 – Macintosh (2006-2020)
Samsung ARM – iPhone (2007-2009)
Apple ARM – iPhone (2010-Present)
Apple ARM – Macintosh (2020-Present)
Apple currently redesigns their CPUs based on workload over time – Image Processing / Audio / Video / Gaming / Artificial Intelligence

## Slide 74: Reading: Post-Risc Architecture
https://cse.msu.edu/~enbody/postrisc/postrisc2.htm

## Slide 75: Reading: Intel 4004
https://www.4004.com/
http://e4004.szyc.org/
http://e4004.szyc.org/iset.html
http://e4004.szyc.org/emu/

## Slide 76: http://e4004.szyc.org/iset.html

## Slide 77: http://e4004.szyc.org/emu/

## Slide 78: WASM – Web Assembly
There is a machine language emulator built into browsers called Web Assembly
For a wide range of software, compiling to WASM and running in JavaScript is enough
WASM is a different syntax than most Assembly languages – but it still compiles to a binary-machine code
C Programming for Everybody (www.cc4e.com) C Playground compiles C to WASM and then runs the WASM in the user's browser

## Slide 79: WASM Hello World
;; Hello World WASM Example
(module
(import "console" "log" (func $log (param i32 i32)))
(memory 1)
(data (i32.const 0) "Hello, World!")
(func $main (result i32)
(call $log (i32.const 0) (i32.const 13))
(i32.const 42)
)
(export "main" (func $main))
)
00000000: 00 61 73 6d 01 00 00 00 01 0a 02 60 02 7f 7f 00 |.asm.......`....|
00000010: 60 00 01 7f 02 0f 01 07 63 6f 6e 73 6f 6c 65 03 |`.......console.|
00000020: 6c 6f 67 00 00 03 02 01 01 05 03 01 00 01 07 11 |log.............|
00000030: 02 06 6d 65 6d 6f 72 79 02 00 04 6d 61 69 6e 00 |..memory...main.|
00000040: 01 0a 0c 01 0a 00 41 00 41 0d 10 00 41 2a 0b 0b |......A.A...A*..|
00000050: 13 01 00 41 00 0b 0d 48 65 6c 6c 6f 2c 20 57 6f |...A...Hello, Wo|
00000060: 72 6c 64 21 |rld!|

## Slide 81: Summary
Fetch-Decode-Execute (a.k.a. Fetch-Execute-Cycle)
Look at the Intel x86 and ARM processor families
Explored the CDC8512 architecture, instruction set, assembly and machine languages
Explored an increasing use of in-browser emulators for games and other applications
Looked at CPU Evolution over time
Looked back at the Intel 4004
Looked forward at Web Assembly (WASM)

## Slide 82: Acknowledgements / Contributions
These slides are Copyright 2025- Charles R. Severance (online.dr-chuck.com) as part of www.ca4e.com and made available under a Creative Commons Attribution 4.0 License. Please maintain this last slide in all copies of the document to comply with the attribution requirements of the license. If you make a change, feel free to add your name and organization to the list of contributors on this page as you republish the materials.
Initial Development: Charles Severance, University of Michigan School of Information
Insert new Contributors and Translators here including names and dates
Continue new Contributors and Translators here